## Slide 1: 西门子Mentor DRS360 AD LoLa介绍1 中国区ABU工程技术中心-侯勇
Realize innovation.
Restricted © Mentor – A Siemens Business 2019

## Slide 2: DRS360™ 四大IP 之： LoLa低延迟数据处理框架
LoLa低延迟数据通讯框架
LoLa (Low Latency framework)

## Slide 3: DRS360™四大IP 之：LoLa - 软件架构图
LoLa Build
Framework System Description Language
LoLa Pkg B
Component B
FCDL
FTDL
Algorithm source
…
LoLa Pkg Z
Component Z
FCDL
FTDL
Algorithm source
LoLa Pkg A
Component A
FCDL
FTDL
Algorithm source
User Space
Cmp A Interface
System Runtime Instance
LoLa Code Generator
Cmp B Interface
Cmp Z Interface
System Runtime Instance
…
Generated Code
LoLa core runtime
LoLa core runtime
Lola RTOS Abstraction
LoLa POSIX Abstraction
LoLa transport
Middle ware
Real Time OS
Linux
CPU1
GPU
CPU2
FPGA IP 1
FPGA IP N
…
CPU3
CPU4
OS
HW

## Slide 4: DRS360™四大IP 之：LoLa：自动生成代码 Auto generated Code
  自动生成代码 Code generator：帮助用户快速生成代码，用户专注于自己算法实现
特点一
Define system by high level Language
特点二
Package components
LoLa building environment
Component implementation
高级描述语言
利用高级描述语言来定义用户特定的系统。
LoLa Domain Specific Language is an essential part of the framework. It allows user toexpress his intentions at a high level and generate C/C++14 code out of it. The generatedcode contains headers and source files.
Support namespacing in high level language
Support “Msg ref” instead of msg files in ROS
Default initialization of variables within the FTDL
打包和集成
通过FPKG(Framework Package descriptor)可以把每个应用模块打包，以便生成lib，方便集成
编译环境
Ship convenience macros to generate code from high level domain language
Create the build targets
Facilitate integration of different components through the encapsulation of include and link paths within the CMake targets.
用户算法实现
LoLa 自动生成的代码已经包含message transport等基础功能，用户只需要在在这个shell下专注于自己的算法实现。
特点四
特点三

## Slide 5: LoLa: Hello world Node: Auto generate code-1
Interface files
Source files
Generate interface packages(*ifce) by *.fpkg
Generate node app
using hello_world_demo.fsdl

## Slide 6: LoLa: Hello world Node: Auto generate code-2
Interface files
Source files
$:../drs360_all/application/lola_demo/demos/CMakeLists.txt
################################### packages ########################
lola_generate_interface(SOURCE hello_world_demo/interface/distance_reading.fpkg
TARGET_LIB hello_world_demo_distance_reading_ifce)
lola_generate_interface(SOURCE hello_world_demo/interface/console.fpkg
TARGET_LIB hello_world_demo_console_ifce)
lola_generate_interface(SOURCE hello_world_demo/interface/sensor_fusion.fpkg
TARGET_LIB hello_world_demo_sensor_fusion_ifce
DEPENDS
hello_world_demo_console_ifce
hello_world_demo_distance_reading_ifce
bsp_trace_ifce)
lola_generate_interface(SOURCE hello_world_demo/interface/perception.fpkg
TARGET_LIB hello_world_demo_perception_ifce
DEPENDS
hello_world_demo_sensor_fusion_ifce)
################################# hello_world C demo ###################
… …
drs360_add_node_app(hello_world_demo_c
FSDL hello_world_demo/interface/hello_world_demo.fsdl
ONLY_C_LIB
IFCE_DEPENDS
hello_world_demo_perception_ifce
hello_world_demo_sensor_fusion_ifce
hello_world_demo_console_ifce
bsp_trace_ifce
……

## Slide 7
convert

## Slide 8: LoLa: LoLaMessage: message pool init and allocate-1

## Slide 9: LoLa: LoLaMessage: message structure
messagegHeader
Message data
LoLaMessage : Message Header + payload
E.g.:Camera message (AutoGened from camera_message.ftdl )

## Slide 10: LoLa: Hello World: lola_init()

## Slide 11: LoLa: Hello World: lola_run()

## Slide 12: LoLa: Hello World - Startup
One Process (node) including
Msg Dispatcher thread,
Console thread,
System Reactor thread

## Slide 13: LoLa Message: send message: outPorts
Using outPorts index, route to the proper component handler
User defined port

## Slide 14: LoLa Message: Handle message: inPorts
Route to the proper message handler using inPorts
User defined port
Global port

## Slide 15: LoLa Message data structure-2
Pool ID is generated in hello_world_demo.c
Initialize the msgId