## Slide 1: Mentor, A Siemens Business
October 11th , 2018
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.
R-Car Gen3 Remote Update

## Slide 2: Objectives
Simplify firmware flashing on Renesas R-Car Gen3 boards (ATF, u-boot, OP-TEE) – no MiniMonitor, no DIP switch handling
Remote full system update (Firmware and Linux)
Improved image versioning and management

## Slide 3: Proposed solution
Framework for remote full-system update (file system + firmware):
Remote update server: hawkBit
Software update for Linux embedded system: SWUpdate
Firmware flashing, patched OP-TEE OS and static TA: flash_app

## Slide 4: 1. SWUpdate
https://github.com/sbabic/swupdate
Image based update application
Supports signed images, single/dual copy, local/remote updates, u-boot, …
Straight-forward Yocto Project integration (meta-swupdate)
  https://wiki.yoctoproject.org/wiki/System_Update#babic.27s_SWUpdate
Configurable update images (sw-description + CPIO archive)
Various handler plugins (raw, file, archive, scripts …)
Already used by Siemens and Mentor Graphics PBU
  https://stash.alm.mentorg.com/projects/MEL/repos/mel-meta-mentor-swupdate/browse

## Slide 5: SWUpdate (2)
.swu images: simple CPIO archives
sw-description: configures the update parameters (JSON)
  FILES="sw-description core-image-h3ulcb.ext4 update.sh“
  for i in $FILES; do echo $i; done | cpio -ov -H crc > update-image-minimal.swu
Update intefaces
  Locally triggered update
    swupdate –i /path/update-image-minimal.swu
  Web server running on the target
    swupdate –w “-r </www_dir>”
  Download from HTTP
    swupdate –d <url>/update-image-minimal.swu
  Use suricatta & hawkBit
    swupdate -u “<suricatta options>

## Slide 6: 2. Eclipse hawkBit
https://www.eclipse.org/hawkbit/
“hawkBit is an domain independent back-end framework for rolling out software updates to constrained edge devices as well as more powerful controllers and gateways connected to IP based networking infrastructure”
swupdate contains a daemon called Suricatta to work with hawkBit
REST APIs available for pretty much everything
Support for scheduled updates, complex rollout mechanisms, targets filtering, software distributions management, …

## Slide 7: Eclipse hawkBit (2)

## Slide 8: 3. flash_app
https://stash.alm.mentorg.com/projects/SOCRENRCAR/repos/rcar-platform-tools/browse/rcar_flash_update
Challenge: Hyper Flash not visible from Linux!
Solution: have the OP-TEE OS flash the firmware images

## Slide 9: flash_app (2)

## Slide 10: So, how is that working?

## Slide 11: Pros
Straight-forward integration with a remote update server
Configurable update images
Complete local/remote system update (bl2, bl31, cert_header, boot_params, u-boot, optee-os, kernel, file system)
Sygned/encrypted update images supported

## Slide 12: Challenges
Recovery mechanisms
Tied to the patched OP-TEE OS (hyperflash) and TA (MMC)
Currently relying on u-boot 18.03 envtools to switch active boot partition and report update status
No interactive remote update on the target side currently supported

## Slide 13: Next steps
Add Integrity and Security support
Add full swupdate image build in Yocto
Secure OP-TEE OS flasher application
Add support for image signing and encryption
Recovery mechanisms

## Slide 14: Next steps (2)
Drawlines for a roll back mechanism:
IPL A side – recovery branch (read only)
IPL B side – working branch
When BootROM integrity check fails or IPL detects a halt, the roll back mechanism is triggered

## Slide 15
Thank you