Video4Linux: Supporting SoCs
Hans Verkuil
Cisco Systems

---
Typical Consumer Hardware

---
OMAP3 ISP
SoC HW: TI OMAP3 ISP
CSI-1
CSI-2
Parallel
Control signals
Bridge lane Shifter
CCDC (Video Processing Front End)
Previewer
Resizer
H3A
HIST
VPBE
Statistics Collection
Shared Buffer Logic
MMU
Interconnect Bus
Courtesy of Texas Instruments

---
SoC HW: TI OMAP3 Previewer
Courtesy of Texas Instruments

---
SoC HW: OMAP3 Display Controller
DSS
Palette
GFX
TDM
Overlay 1
Color
Conversion
Scaling
Color Key
VID-1
LCD
TFT
Background color
Overlay 2
Color Key
TV out
Encoder
Video
DAC
TV
Color
Conversion
Scaling
VID-2
Video
DAC
Bkground color
Overlays/Pipeline
Overlays Manager
Display Sub System
Courtesy of Texas Instruments

---
SoC Video Devices
- Very complex devices.
- Multiple video and graphics streams.
- Flexible video stream routing.
- Applications require much more control.
- Digital cameras, mobile phones, media players, TVs, surveillance applications, video conferencing, in-flight entertainment, etc., etc.
- Since the V4L2 API does not support these advanced devices, SoC manufacturers make their own custom drivers.

---
SoC Support Developments
- Initial talks with Texas Instruments Spring/Summer 2008.
- First RFC July 2008.
- Discussed during the Linux Plumbers Conference in August 2008.
- Core framework required: mostly done by 2.6.30 (June 2009).
- Organized a v4l-dvb mini-summit during the Linux Plumbers Conference in September 2009 with participants from Texas Instruments, Intel, Nokia, Samsung and independent v4l-dvb developers. Agreed on how to proceed with V4L SoC support.
- Brainstorm meeting to discuss memory handling (videobuf) in March 2010.
- Mini-summit in June 2010 in Helsinki.

---
Results from 2009/10 mini-summits
- Need better V4L2 driver framework to provide solid foundation for the other tasks. (Mostly done)
- Need new timings API for HDTV and other high-definition sources and sinks. (Done)
- Need standard event passing API. (Done)
- Need new core control framework. (Done)
- Need better buffer pool management APIs. (Work started)
- Need support for multi-planar framebuffers. (Mostly done)
- Replacement for videobuf framework. (In progress)
- Need a Media Controller. (Mostly done)

---
HDTV Timings API
- Has presets for the common standards (e.g. 720p30, 1080p60, etc.)
- Can get/set/query the preset.
- If the hardware allows it, then it can also set custom timings (front & backporch, sync widths, pixelclock).
- Merged in 2.6.33.

---
Events API
- Standard API for V4L2 events.
- Can be used with select() since it arrives as an exception.
- Per-filehandle event queue and event subscription.
- Merged in 2.6.35.

---
Control Framework
- Too much hard work for drivers.
- A lot of code duplication.
- A lot of buggy code.
- Inconsistencies between drivers.
- All controls go through the new framework.
- A driver only needs to supply a s_ctrl function in most cases.
- Future enhancement: expose controls to debugfs.
- Ability to have bridge drivers inherit controls from subdevs.
- Merged in 2.6.36.

---
Off-Topic: RDS & IR & BKL
- RDS = Radio Data System. Provides program name and type, traffic information, etc.
- V4L2 has an API for this, both for receiving and for transmitting.
- It has seen a lot of development recently (Nokia!), driven by the requirements of mobiles with radio support.
- Infrared remote support is now integrated into the kernel and is part of the v4l-dvb subsystem. It still sees a fair amount of development.
- BKL removal: added optional locking to the V4L2 core framework.

---
V4L2 Core Framework
- Created a struct v4l2_device for basic device-global data.
- Created a struct v4l2_subdev to communicate with (usually i2c) sub-devices. Register them with v4l2_device. When v4l2_device is removed, unregister the sub-devices automatically.
- The 'sub-device' concept is an abstract concept: it does not care on what (if any) bus the sub-device is located.
- Ensures a unified API towards sub-devices to make it easy to swap one chip for another.
- Ensures re-use of the same sub-device driver.
- Can also be used to expose internals of the video subsystem of a SoC.

---
V4L2 Core Framework

---
Media Controller
- Modern v4l drivers often also support framebuffer, alsa, i2c, lirc and/or dvb devices, hard to keep track of by applications. Need some central authority to tell apps what is what.
- Many SoCs can reroute the internal videostreams. E.g. capture from a sensor and do memory-to-memory resizing, or send the sensor output directly to the resizer.
- Apps writing for SoCs want much more control about the various components of the device. A way is needed to provide that control without compromising the normal API which tends to hide complexity from the user.

---
Media Controller
- Create a /dev/mediaX device (X >= 0) that can be used to enumerate the mesh-topology of the device.
- Nodes in the mesh are sub-devices and device nodes. The general name for a mesh node is entity.
- The mc will also enumerate the possible and current links between entities.
- The mc allows you to change the links.
- Some sub-devices will have their own device node for advanced control (/dev/v4l-subdevX).

---
Media Controller
- Current drivers for consumer products can use the mc to let apps discover which alsa device is associated with which v4l device.
- For embedded devices the mc controls the internal data flow of the device.
- For embedded devices the /dev/v4l-subdevX device nodes allow direct control of the advanced and hardware-specific features of sub-devices.
- For each particular SoC a userspace library will be required to use the hardware optimally. This allows us to keep the kernel driver simple.

---
TI OMAP3 ISP: Media API
Courtesy of Laurent Pinchart

---
TI OMAP3 ISP: Block Diagram
CSI-1
CSI-2
Parallel
Control signals
Bridge lane Shifter
CCDC (Video Processing Front End)
Previewer
Resizer
H3A
HIST
VPBE
Statistics Collection
Shared Buffer Logic
MMU
Interconnect Bus
Courtesy of Texas Instruments

---
Memory Handling, Memory Pool
- Existing videobuf framework is very bad code. Replace with videobuf2. Proper separation between buffer ops and memory ops. (In progress)
- Prevent unnecessary cache and memory locking operations. New caching flags were proposed, nothing implemented yet.
- Allow easy transfer of buffers from one video device node to another. Pending videobuf2 integration.
- Contiguous Memory Allocator. (In progress, more research still needed)
- Have a global pool of buffers. Still needs more R&D.
- Multiplanar support (Mostly done)
- Mem-to-Mem devices (Done)

---
Timeline
- Timings API went into 2.6.33.
- Event API went into 2.6.35.
- Control framework went into 2.6.36.
- videobuf2 is scheduled for 2.6.38.
- Multiplanar is scheduled for 2.6.38.
- Memory pool: not yet known.
- Media Controller is scheduled for 2.6.38.
- Improving the V4L2 driver framework is ongoing work.

---
Questions?
e-mail:
hverkuil@xs4all.nl
linux-media mailinglist:
http://www.linuxtv.org/lists.php