## Slide 1
CAN interface testing on Beaglebone
Document ID: ESS-CAN-BB-01
Version: 1.0
Author: Rajam AP & Hema Priya B
Embedded Division, Accel Frontline Ltd,

## Slide 2: Introduction
The Controller Area Network (CAN) is a serial communications protocol which efficiently supports distributed real-time control with a high level of security.
CAN interface is being heavily used in automotive domains
This presentation shares the experience of configuring the CAN interface on the most widely used Beagle bone board from TI .
The Beaglebone board is based on AM335x Processor and has support for CAN interface that is based on Bosch CAN 2.0B protocol specification and supports bitrates up to 1 Mbit/s.

## Slide 3: References
To bring up CAN interface, refer to following links:
http://e2e.ti.com/support/dsp/sitara_arm174_microprocessors/f/791/t/154560.asx
http://processors.wiki.ti.com/index.php/AM335X_DCAN_Driver_Guide#CAN_Utilities
CAN Utilities can be downloaded from the following links :
pkgs.fedoraproject.org/repo/pkgs/iproute/iproute2-2.6.39.tar.gz/8a3b6bc77c2ecf752284aa4a6fc630a6/iproute2-2.6.39.tar.gz
www.pengutronix.de/software/libsocketcan/download/libsocketcan-0.0.8.tar.bz2
http://www.pengutronix.de/software/socket-can/download/canutils/v4.0/

## Slide 4: OBJECTIVE
Objective of this presentation is to share information on steps we followed to enable and test the CAN interface on Beagle bone.
Steps followed in brief
  Implementation plan
  Hardware setup
  Kernel source modification
  Kernel configuration
  Addition of CAN utilities to target file system
  Testing of CAN interfaces using CAN utils
Following slides cover detailed description of above steps.

## Slide 5: Implementation plan
The following block diagram depicts the implementation plan for the CAN interface testing:

## Slide 6: Hardware setup
Beaglebone board has provision of connecting the CAN interface through the P9 connector pins.
Reference: Beaglebone Rev A5 System Reference manual (BONESRM_A5.pdf).
The board supports two CAN interfaces D_CAN0 and D_CAN1.
An add-on board was made for each of the D_CAN interface to connect the hardware pins from the board to a CAN transceiver and then onto a DB9 port.

## Slide 7: Hardware setup contd …
  We used TI’s SN65HVD230D – referred as VP230 – as CAN transceiver
  The schematics of the add-on boards for bringing out the CAN interfaces is given below :

## Slide 8: Linux kernel Source modification
The following points discuss the software changes required for using the D_CAN interfaces on the board
Base kernel source (linux-3.2-psp04.06.00.07.sdk) is modified to enable D_CAN device support on Beagle bone.
The following link helps to modify the kernel source to bring up can0 and can1 interfaces:
http://e2e.ti.com/support/dsp/sitara_arm174_microprocessors/f/791/t/154560.asx
Source code modified files are board-am335x_evm.c and mux33xx.c which are located in directory: <linux_src_dir/arch/arm/mach-omap2/>

## Slide 9: Linux Kernel Configuration
To enable/disable CAN driver support, we started the Linux Kernel configuration tool:
  Under Linux kernel source directory issued following command:
$ make ARCH=arm CROSS_COMPILE=arm-arago-linux-gnueabi- menuconfig
Linux Kernel Configuration dialog box appears:
  In that , selected Networking support from the main menu.
... ... Power management options --->
[*] Networking support --->
Device Drivers --->
File systems --->
  Under Networking support, selected CAN bus subsystem support as shown here:
…
Networking options -
[ ] Amateur Radio support -
<*>Can bus system support -
IRDA (infrared) subsystem support -
….

## Slide 10: Linux Kernel Configuration Contd ..
Selected Raw CAN Protocol & Broadcast Manager CAN Protocol as shown here:
.....
--- CAN bus subsystem support
<*> Raw CAN Protocol (raw access with CAN-ID filtering)
<*> Broadcast Manager CAN Protocol (with content filtering)
<*>CAN Device Drivers --->
Selected Bosch D_CAN devices and then selected the following options:
<> Virtual Local CAN Interface (vcan)
<*> Platform CAN drivers with Netlink support
[*] CAN bit-timing calculation
< > TI High End CAN Controller
< > Microchip MCP251x SPI CAN controllers .
< > Philips/NXP SJA1000 devices --->
< > Bosch C_CAN devices --->
<*> Bosch D_CAN devices ---> <*> Generic Platform Bus based D_CAN driver
CAN USB interfaces --->
.....
Note: "CAN bit-timing calculation" needs to be enabled to use “CAN “utility to set CAN bitrate.

## Slide 11: Addition of CAN utilities to target file system
After building the kernel, to test and use the CAN interfaces, CAN utilities were deployed.
We followed the below link for building CAN utilities:
http://processors.wiki.ti.com/index.php/AM335X_DCAN_Driver_Guide#CAN_Utilities
For testing CAN we commonly use the cansend /cangen and candump utilities to send and receive packets via CAN module.
To configure the CAN interface, net link standard utilities are used and this requires iproute2 utilities. The following procedures have been carried out to build iproute2 , libsocketcan and CAN-utils with the help of above link.
Note : All the three packages have been configured under the same directory .

## Slide 12: Addition of CAN utilities to target file system contd.,
Steps we followed to build CAN utilities :
Downloaded IPROUTE 2.6.39 source code in from the link mentioned below: http://pkgs.fedoraproject.org/repo/pkgs/iproute/iproute2-2.6.39.tar.gz/8a3b6bc77c2ecf752284aa4a6fc630a6/iproute2-2.6.39.tar.gz
Ip cross compilation:
  Modifications :
  Makefile modifications are needed for cross compiling the source for ARM .
  Inside a Makefile,
  Commented these variables from top Makefile , and set appropriate environment
  variables for building.
  DESTDIR
  DBM_INCLUDE
  CC
  Note: Do not build arpd
  On console, under iproute2 src directory,
  $ cp misc/Makefile{,.orig}
  $ sed '/^TARGETS/s@arpd@@g' misc/Makefile.orig > misc/Makefile

## Slide 13: Addition of CAN utilities to target file system contd.,
Set the Environment variables as :
export GNUEABI=arm-arago-linux-gnueabi
export CC=$GNUEABI-gcc
export LD=$GNUEABI-ld
export NM=$GNUEABI-nm
export AR=$GNUEABI-ar
export RANLIB=$GNUEABI-ranlib
export CXX=$GNUEABI-c++
    export PREFIX=/usr2/BBV1/build/can/_install ( <Path to where the binaries are to be installed>)
    export CROSS_COMPILE_PREFIX=$PREFIX
    export DBM_INCLUDE=/usr/include
    export INCLUDES=/usr/include
    export DESTDIR=${PREFIX}/

## Slide 14: Addition of CAN utilities to target file system contd.,
Configuration:
  $ ./configure --host=arm-arago-linux --prefix=$PREFIX --enable-debug
Build & Install:
  $ make
  $ make install
Copied the ip executables to the /sbin directory of the root-file system.
Note: The execution and result of this iproute2 configuration is shown in the next slide which shows an error like “iptables modules directory not found”. The error can be ignored and does not have impact on CAN utilities working as per our experience.

## Slide 15: Addition of CAN utilities to target file system contd.,
Change to the directory where iproute is downloaded into your system. In this case it is: /usr2/BBV1/build/can/iproute2-2.6.395 and execute the configuration command:
  $ ./configure --host=arm-arago-linux --prefix=$PREFIX --enable-debug
  After this command is executed, you will see the following output on the terminal as mentioned below:
  TC schedulers
  ATM no
  IPT using iptables
  iptables modules directory: not found!
  Then proceeded with the command “make “ and “make install” .

## Slide 16: Addition of CAN utilities to target file system contd.,
Libsocketcan cross compilation:
Downloaded the source code from the link:
http://www.pengutronix.de/software/libsocketcan/download/libsocketcan-0.0.8.tar.bz2
Environment Variables:
Using the same environment variables compiled for iproute2 .
Configuration:
$ ./configure --host=arm-arago-linux --prefix=$PREFIX --enable-debug
Build and Install:
$ make
$ make install

## Slide 17: Addition of CAN utilities to target file system contd.,
CAN-utils cross compilation:
Downloaded the source code for CANutils from the link :
http://www.pengutronix.de/software/socket-can/download/canutils/v4.0/
Note: The CAN-utils version, we used is 4.0.6
Environment variables, we set based on our build directory structure:
export GNUEABI=arm-arago-linux-gnueabi
export CC=$GNUEABI-gcc
export LD=$GNUEABI-ld
export NM=$GNUEABI-nm
export AR=$GNUEABI-ar
export CXX=$GNUEABI-c++
export PREFIX=/usr2/BBV1/build/can/install //User-defined
export CROSS_COMPILE_PREFIX=$PREFIX
  export PKG_CONFIG_PATH=$PWD/../libsocketcan-0.0.8/config

## Slide 18: Addition of CAN utilities to target file system contd.,
  export LD_LIBRARY_PATH="../usr2/BBV1/build/can/lib:${LD_LIBRARY_PATH"
  export LD_RAN_PATH="../usr2/BBV1/build/can/lib:${LD_RAN_PATH}"
  export LDFLAGS="-Wl,--rpath -Wl,/usr/local/lib -L/usr2/BBV1/build/can/usr2/BBV1/build/can/lib"
  export INCLUDES="-I/usr/include -I/usr2/BBV1/build/can/libsocketcan-0.0.8/include“
  Configuration:
  $ ./configure --host=arm-arago-linux --prefix=$PREFIX --enable-debug
  Build and Install:
  $ make
  $ make install
  Then, the built libraries and binaries are taken to the /lib and /sbin directory of root-file system of Beagle bone.

## Slide 19: Testing of CAN interface
After building the kernel and root-file system with CAN utilities, we proceeded with the following steps to test the CAN interface on Beaglebone board with the hardware setup we have mentioned it before(slide 5) .
On board,
  First ,we need to configure and start both the CAN interfaces, can0 and can1, using CANutils :
  $ canconfig can0 bitrate 50000 ctrlmode triple-sampling on
  $ canconfig can0 start
  $ canconfig can1 bitrate 50000 ctrlmode triple-sampling on
  $ canconfig can1 start
  Note:
  1. A command “ifconfig” is used to check for device interfaces up on Beagle bone
  2. The usage of CAN utils executables can be known in detail by using a command --help after CAN utils executable (e.g. cansend --help).

## Slide 20: Testing of CAN interface contd.,
      Next, any one of the interface is made to run as back end process in receiving mode. Here, we have chosen can1 interface as a receiver,
        $ candump can1 –d
      The option “-d” in candump command indicates that this runs as a back end process candump is also provided with filtering option.
      Now, we started to transmit the test data/frames from can0 interface using cansend utils. For e.g.
      $ cansend can0 0x11 0x22 0x33 0x44 0x55 0x66 0x77 0x88
      The transmitted data/frames are received by can1 interface which is in receiving mode. The result of the above testing is shown in the next slide.
      After adding the root file system to the board ,we can know the statistics of can0 or can1 interface , cat /proc/net/dev or cat /proc/net/can/stat is used.

## Slide 21: Testing result of CAN interface
Please press Enter to activate this console .
# canconfig can0 bitrate 10000 ctrlmode triple-sampling on
can0 bitrate: 10000, sample-point: 0.875
can0 ctrlmode: loopback[OFF], listen-only[OFF], tripple-sampling[ON],one-shot[O]
# canconfig can0 start
[ 83.364250] d_can d_can.0: can0: setting CAN BT = 0x21c15
can0 state: ERROR-ACTIVE
# canconfig can1 bitrate 10000 ctrlmode triple-sampling on
can1 bitrate: 10000, sample-point: 0.875
can1 ctrlmode: loopback[OFF], listen-only[OFF], tripple-sampling[ON], one-shot[ON]
# canconfig can1 start
[ 93.712250] d_can d_can.1: can1: setting CAN BT = 0x21c15
can1 state: ERROR-ACTIVE
# candump can1 -d
interface = can1, family = 29, type = 3, proto = 1
# cansend can0 0x11 0x22 0x33 0x44 0x55 0x66 0x77 0x88
interface = can0, family = 29, type = 3, proto = 1
# cat /proc/net/dev
  Inter-| Receive | Transmit
  face |bytes packets errs drop fifo frame compressed multicast|bytes packets errs drop fifo colls carrier compressed
  lo 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
  can1 8 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0
  can0 0 0 0 0 0 0 0 0 8 1 0 0 0 0 0 0
  eth0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 22: Debugging support
Basic debugging:
User can test the addition of CAN interfaces in kernel by viewing the devices in the target system under the network device directory.
This can be done using the command cat /proc/net/dev/ on terminal, which should give following output.
  # cat /proc/net/dev
  Inter-| Receive | Transmit
  face |bytes packets errs drop fifo frame compressed multicast|bytes packets errs drop fifo colls carrier compressed
  lo 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
  can1 8 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0
  can0 0 0 0 0 0 0 0 0 8 1 0 0 0 0 0 0
  eth0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
If the devices are not seen in this directory , then kernel source code must be checked for proper initialization and configuration.

## Slide 23: Debugging support contd..,
Once the devices are shown in the kernel, the CAN-utils executables can be used for setting up IP network over the CAN driver. This is done by executing “canconfig” command as mentioned in slide 19.
The availability CAN as network interface can be checked with “ifconfig” command on terminal as shown below:
  can0 Link encap:UNSPEC HWaddr 00-00-00-00-00-00-00-00-00-00-00-00-00-00-0
  UP RUNNING NOARP MTU:16 Metric:1
  RX packets:0 errors:0 dropped:0 overruns:0 frame:0
  TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
  collisions:0 txqueuelen:10
  RX bytes:0 (0.0 B) TX bytes:0 (0.0 B)
  Interrupt:52
  can1 Link encap:UNSPEC HWaddr 00-00-00-00-00-00-00-00-00-00-00-00-00-00-0
  UP RUNNING NOARP MTU:16 Metric:1
  RX packets:0 errors:0 dropped:0 overruns:0 frame:0
  TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
  collisions:0 txqueuelen:10
  RX bytes:0 (0.0 B) TX bytes:0 (0.0 B)
  Interrupt:55

## Slide 24: Debugging support contd..,
Debugging the data transmission:
If CAN is seen as network interface but if the communication is not going through and packets are not received at the other interface, user can test each CAN interface in loopback mode
Loopback configuration:
  $ canconfig can0 bitrate 50000 ctrlmode triple-sampling on loopback on
  $ canconfig can0 start
  Set the same interface in loopback mode :
  $ candump can0 –d
  Then, try sending CAN frames in an infinite loop using cansend.
  $ cansend can0 –l 0x00 0x00 0x00 0x00 0x00 0x00 0x00 0x00
On h/w side, user need to check for activity in TX pin in loopback mode
If the activity is not seen in the pin, then there is issue in hardware.
Sample result of can0 interface in loopback mode is displayed below .

## Slide 25: Debugging support contd.,
Result of can0 interface in loopback mode :
# canconfig can0 bitrate 10000 ctrlmode triple-sampling on
  can0 bitrate: 10000, sample-point: 0.875
  can0 ctrlmode: loopback[OFF], listen-only[OFF], tripple-sampling[ON],one-shot[O]
  # canconfig can0 start
  [ 83.364250] d_can d_can.0: can0: setting CAN BT = 0x21c15
  can0 state: ERROR-ACTIVE
  # candump can0 –d
  interface = can0, family = 29, type = 3, proto = 1
  # cansend can0 0x11 0x22 0x33 0x44 0x55 0x66 0x77 0x88
  interface = can0, family = 29, type = 3, proto = 1
  <0x01> [8] 11 22 33 44 55 66 77 88
  <0x01> [8] 11 22 33 44 55 66 77 88

## Slide 26: Conclusion
We conclude that both D_CAN0 and D_CAN1 interfaces can be brought up by enabling D_CAN device driver support in kernel and by adding CAN utilities to the root file system of the board.
By connecting the two D_CAN interfaces with CAN transceiver, we are able to test the communication between the two interfaces successfully.

## Slide 27: Thank-you for your time