## Slide 1: A Deep Dive into Image Processing for i.MX 6 Application Processors
External Use
TM
FTF-CON-F0119
Oliver Brown | Senior Software Engineer
A P R . 1 0 . 2 0 1 4

## Slide 2: Agenda
Introduction
IPUv3 – system overview
IPUv3 – fundamentals
IPU & the iMX Linux BSP
Use case examples / tips
External Use 15

## Slide 3: Introduction
IPU (Image processing Unit) is present on most of i.MX products
IPUv1 was 1st introduced on i.MX31 and upgraded on i.MX35
IPUv3 is a family of IPs that are present on MX37, i.MX51, i.MX53, i.MX6Q/D/DL
External Use 15

## Slide 4: Introduction
This presentation will describe IPUv3 on i.MX5 and i.MX6.
The slides are based on i.MX6
IPUv3 architecture is common for all products
The differences between one product to another are on
  Processing speed (from 133Mhz to 264Mhz)
  The modules included (CSI, VDI, ISP etc)
  The connectivity options and interfaces (HDMI, LVDS, MIPI etc)
External Use 15

## Slide 5: Introduction
The following slide set is based on past versions of IPUv3
  The slides used for the i.MX51’s NPI training can be found on:
    http://compass.freescale.net/doc/195331621/0201_IPUv3EX_In_MX51.ppt
  The slides used for the i.MX53’s NPI training can be found on:
    http://compass.freescale.net/livelink/livelink/218704608/iMX53_IPUv3M.ppt?fun c=doc.Fetch&nodeid=218704608
  The slides used for the i.MX6’s NPI training can be found on:
    http://compass.freescale.net/livelink/livelink/224514161/Day2-1-iMX6_Dual- Quad_NPI_Training_-_IPU.pptx?func=doc.Fetch&nodeid=224514161
External Use 15

## Slide 6: IPUv3 resources
Freescale Internal Links
IPU on Compass
  http://compass.freescale.net/go/ipu
  http://compass.freescale.net/go/ipudes
IPUv3 code examples for MX6/Q
  http://compass.freescale.net/livelink/livelink?func=ll&objId=222977460&objAction=browse&viewType=1
IPUv3 code examples
  http://compass.freescale.net/go/189478969
IPUv3 users mail list
  IPUFORUM@freescale.com
External Links
  https://community.freescale.com/community/imx
External Use 15

## Slide 7
Video/Graphics System in i.MX6 D/Q
External Use 15

## Slide 8: Video & Graphics System in i.MX6 D/Q
Full HW Support –> Multiple Advantages
The CPU does not have to touch pixels
–> available to run application
Optimized data path –> reduced DDR load
–> complex use cases with only 32-bit DDR memories
Lower power consumption (because of both aspects above)
VPU
(Video Processing Unit)
Video encoding and decoding
GPUs
(Graphics Processing Units)
Graphics generation
IPUs
(Image Processing Unit)
Connectivity to relevant devices
Image processing: conversions, enhancement…
Synchronization and control
Video Sources
Displays
Interface Bridges
LVDS, HDMI, MIPI
DCICs
Display Content Integrity Check
External Use 15

## Slide 9: Video/Graphics Subsystem in i.MX6 D/Q
i.MX6 Dual/Quad
ARM CPU
IRAM
IPUs
External Memories
GPUs
VPU
Bridges
Displays
Video Sources
Memory Interface
Data Control
DCICs
VDOA
External Use 15

## Slide 10: Multimedia Processing Chain
Image Signal Processing
  Bayer -> YUV conversion
  Image quality
enhancement
  Camera corrections
Image Conversions
  De-interlacing
  Resizing (resolution adjustment)
  Rotation & Inversion
  Color Space Conversion
  Pixel Format Conversion (packing…)
Display Enhancement:
  Color adjustments and gamut mapping
  Gamma correction and contrast stretching
  Compensation for low- light conditions and backlight reduction
Combining with Audio
Image Sensor Display
Camera Preview
Memory
Communication
Network
Separation from Audio
Image Conversions
Compression
Audio Compression
Audio De-compression
De-blocking De-ringing
Display Enhancement
Image Conversions
De-compression
Image Signal Processing
Video/Graphics
Combining
Graphics Generation
External Use 15

## Slide 11: imedia Processing Chain – Implementation
Mult
Camera
Image Sensor
Combining with Audio
Display
Image Processing Unit (IPU)
Camera Preview
Separation from Audio
Image Conversions
Compression
Video Processing Unit (VPU)
Audio Compression
Audio De-compression
De-blocking De-ringing
Display Enhancement
Image Conversions
De-compression
Image Signal Processing
Comprehensive HW support:
Video/graphics fully handled by IPU, VPU and GPU.
-> The CPU does not have to touch pixels
HW Accelerated
Video/Graphics
Combining
Graphics Generation
Graphics Processing Units (GPUs) And ARM
Memory
Communication
Network
ARM
External Use 15

## Slide 12
Display Support
External Use 15

## Slide 13: i.MX37, i.MX51, i.MX53, i.MX6 D/Q – Display Support
How to calculate the display resolution?
FW = Frame Width
FH = Frame Height
FPS = Frame rate (fps)
BI = Blanking interval
  Provided in the display’s DS up to 35% (1.35).
  Use min values
The pixel clock [MHz] is calculated according to:
F = FW X FH X FPS X BI
Few things to consider:
  Data format (pixel per clock?)
  Display’s clock source (DI#_CLK_EXT bit)
  The load on the display controller (DC)
External Use 15

## Slide 14: i.MX37, i.MX51, i.MX53, i.MX6 D/Q – Display Support
Feature |  | i.MX51 (IPUv3EX) i.MX37 (IPUv3D) | i.MX53 (IPUv3M) | i.MX6 D/Q (2 x IPUv3H)
Throughput | # of outputs | 2 |  | 4
 | Pixel clock rate | Up to 133 MHz | Up to 200 MHz | Up to 266 MHz per IPU
 | Resolution (@ 60 Hz) | WXGA+ (1600x900) 720p (1280x720) + SVGA (800x600) | WUXGA (1920x1200) 1080p (1920x1080) + WVGA (800x480) | 2 x 4XGA (2048x1536) 2 x [1080p + WXGA (1280x720)]
Interfaces | Parallel | Two ports 24 bits + 18 bits | Two ports 24 bits + 24 bits | 
 |  | Synchronous (for display refresh) and asynchronous (to memory) Very flexible - glue-less connection to RAM-less displays, display controllers, and TV encoders. |  | 
 | LVDS | No | Two channels; consumer version (multiple pairs); 2x 85 MHz or 170MHz | 
 | HDMI | No |  | One port
 | MIPI/DSI | No |  | One port, 2 lanes x 1 Gbps (non-Automotive)
 | Analog | One port; TV-out i.MX37: SDTV i.MX51: also 720p60 or 1080i/p30 | Also VGA Rate increased to 1080p60 | None (phased out)
Display Content Authentication (CRC) |  | No |  | Yes, for 2 displays
Processing | On-the-fly combining (for high resolution displays) | 2 planes (up to 3 more planes for lower resolutions) |  | For 2 displays, 2 planes for each (6 more planes for lower resolutions)
 | Off-line combining | Up to 20 MP/sec | Up to 200+ MP/sec | Up to 500+ MP/sec
 | Display enhancement | Color adjustment and smart gamut mapping; gamma correction and contrast enhancement Supporting effective proprietary algorithms |  | 
 | Backlight power optimization | Yes; Supporting efficient proprietary algorithms |  | 
External Use 15

## Slide 15: in i.MX6 D/Q (IPUv3H) – Maximal Resolution & Refresh
IPU
Rate
Name | Resolution |  |  |  | Maximal Refresh Rate [Hz]
 | Width | x | Height | Total [MP] | 
VGA | 640 | x | 480 | 0.31 | 666
PAL | 720 | x | 480 | 0.35 | 592
WVGA | 800 | x | 480 | 0.38 | 533
NTSC | 720 | x | 576 | 0.41 | 493
SVGA | 800 | x | 600 | 0.48 | 426
WSVGA | 1024 | x | 600 | 0.61 | 333
XGA | 1024 | x | 768 | 0.79 | 260
HD720 | 1280 | x | 720 | 0.92 | 222
WXGA | 1366 | x | 768 | 1.05 | 195
WXGA+ | 1440 | x | 900 | 1.30 | 158
SXGA | 1280 | x | 1024 | 1.31 | 156
SXGA+ | 1400 | x | 1050 | 1.47 | 139
WSXGA+ | 1680 | x | 1050 | 1.76 | 116
UXGA | 1600 | x | 1200 | 1.92 | 107
HD1080 | 1920 | x | 1080 | 2.07 | 99
WUXGA | 1920 | x | 1200 | 2.30 | 89
9VGA | 1920 | x | 1440 | 2.76 | 74
4XGA | 2048 | x | 1536 | 3.15 | 65
HD1440 | 2560 | x | 1440 | 3.69 | 56
4WXGA | 2560 | x | 1600 | 4.10 | 50
4K x 2K | 4096 | x | 2048 | 8.39 | 25
800 x 480 (WVGA) ~331 Hz |  |  |  | 
1280 x 720 (HD720) ~138 Hz |  |  |  | 
1024 x 768 (XGA) ~161 Hz |  |  |  | 
1920 x 1080 (HD1080) ~61 Hz 2048 x 1536 (4XGA) ~40 Hz |  |  |  | 
Capabilities
  Maximal display resolution: 4096x4096 pixels
  Maximal pixel rate: 264 MP/sec (200MP/sec on MX53, 133MP/sec on MX51)
Display refresh rate
  The maximal refresh rate is: 264M / (W * H * B)
    W*H is the display resolution
    B is a factor >1 reflecting blanking overhead, e.g. as specified by VESA, CEA-861- D, etc.
  The table provides the maximal refresh rates for some typical resolutions
  Usually, the refresh rate is required to be at least 60 Hz, to prevent blinking.
  The blanking overhead factor assumed for the calculation is 1.3.
    The actual factor depends on the display and is often closer to 1, allowing higher resolutions @ 60 Hz (e.g. HD1440).
    For example, for HD1080, the standard specifies B~1.2
  This is the capability of each of the two IPUs, so the total capability of the processor is doubled.
  Note: these rates refer only to screen refresh, gated by the capabilities of the display port. A full use case typically includes additional activities and to confirm its support with a given refresh rate, additional aspects – video processing capabilities, capacity of the memory system, etc. – should be also analyzed carefully.
External Use 15

## Slide 16: IPU in i.MX6 D/Q (IPUv3H) – Dual-Display Capabilities
Notes
  This is the capability of each of the two IPUs, so the total capability of the processor is doubled.
  The maximal pixel clock rate supported by the display ports
    Each display: 220 MHz
    Total: 240 MHz
  For a TV, the clock rate is fixed by the corresponding standards
  For other displays
    The assumed screen refresh rate is 60 Hz
    The blanking overhead – impacting the pixel clock rate – may vary between displays.
The table refers – for concreteness – to the VESA CVT (Coordinated Video Timing) specification
      “Full support”: allowing full blanking (which is typically required for CRTs)
      “Partial support”: allowing only reduced blanking (which is still typically sufficient for digital displays, e.g. LCDs)
  The above table describes only the capabilities of the display ports to perform screen refresh. A full use case typically
includes additional activities and to confirm its support with a given display configuration, additional aspects – video
processing capabilities, capacity of the memory system, etc. – should be also analyzed carefully.
Second Display First Display | SDTV 480i30/576i25 (27 MHz) | WSVGA (1024x600) (44-49 MHz) | HDTV 720p60/1080i30 (74.25 MHz) | WXGA (1366x768) (72-85 MHz) | WSXGA+ (1680x1050) (119-146 MHz) | HDTV 1080p60 (148.5 MHz)
WXGA (1366x768 ~ 1.0 MP; 72-85 MHz) | Full | Full | Full | Full | Full | Full
SXGA (1280x1024 ~ 1.3 MP; 91-109 MHz) | Full | Full | Full | Full | Partial | Partial
SXGA+ (1400x1050 ~ 1.5 MP; 101-122 MHz) | Full | Full | Full | Full | Partial | 
WSXGA+ (1680x1050 ~ 1.8 MP; 119-146 MHz) | Full | Full | Full | Full | Partial | 
UXGA (1600x1200 ~ 1.9 MP; 130-161 MHz) | Full | Full | Full | Partial |  | 
WUXGA (1920x1200 ~ 2.3 MP; 154-193 MHz) | Full | Partial | Partial |  |  | 
9VGA (1920x1440 ~ 2.8 MP; 185-234 MHz) | Partial | Partial |  |  |  | 
4XGA (2048x1536 ~ 3.2 MP; 209-267 MHz) | Partial |  |  |  |  | 
External Use 15

## Slide 17: i.MX6 D/Q Display Ports Muxing
DCIC #0
DCIC #1
LVDS #0
LVDS #1
Parallel
#0
HDMI
Parallel
#1
Lockable control
Lockable control
Six ports
  Two parallel - driven directly by the IPU
  Two LVDS channels - driven by the LVDS bridge
  One HDMI – driven by the HDMI transmitter
  One MIPI-DSI – driven by the MIPI-DSI transmitter
MIPI
DSI • Four simultaneous outputs
  Each IPU has two display ports (DI0 and DI1)
  Therefore, up to four external ports can be active at any given time.
  Additional asynchronous data flows can be sent through the parallel ports and the MIPI-DSI port
Display Content Integrity Check (DCIC)
  For parallel interfaces: probes the I/O loopback (essentially equivalent to probing the external wires)
  For other integrated interfaces (e.g. LVDS): probes the IPU output (essentially equivalent to the inputs to the serializers)
MIPI DSI
IPU #0
DI0 DI1
IPU #1
DI0 DI1
External Use 15

## Slide 18: Max Display Port Resolutions on i.MX6Q/D
MIPI DSI, 2 lanes
− WXGA (1366 x 768) or 720p (1280 x 720)
RGB
− Port 1 – 4XGA (2048 x 1536)
− Port 2 – 4XGA (2048 x 1536)
LVDS
− Single channel – WXGA (1366 x 768) or 720p (1280 x 720)
− Dual channel – UXGA (1600 x 1200) or 1080p (1920 x 1080)
HDMI
− 1080p (1920 x 1080) or 4XGA (2048 x 1536)
Note: Assuming 30% blanking intervals overhead, 24bpp, 60fps
External Use 15

## Slide 19: Connecting a display on the parallel interface
i.MX51 | LCD |  |  |  |  |  |  | 
 | RGB, Signal name (General) | RGB/TV Signal Allocation (Example) |  |  |  |  |  | Smart
Port Name (x=1,2) |  | 16 bit RGB | 18 bit RGB | 24 bit RGB | 8 bit YCrCb | 16 bit YCrCb | 20 bit YCrCb | Signal name
DISPx_DAT0 | DAT[0] | B[0] | B[0] | B[0] | Y/C[0] | C[0] | C[0] | DAT[0]
DISPx_DAT1 | DAT[1] | B[1] | B[1] | B[1] | Y/C[1] | C[1] | C[1] | DAT[1]
DISPx_DAT2 | DAT[2] | B[2] | B[2] | B[2] | Y/C[2] | C[2] | C[2] | DAT[2]
DISPx_DAT3 | DAT[3] | B[3] | B[3] | B[3] | Y/C[3] | C[3] | C[3] | DAT[3]
DISPx_DAT4 | DAT[4] | B[4] | B[4] | B[4] | Y/C[4] | C[4] | C[4] | DAT[4]
DISPx_DAT5 | DAT[5] | G[0] | B[5] | B[5] | Y/C[5] | C[5] | C[5] | DAT[5]
DISPx_DAT6 | DAT[6] | G[1] | G[0] | B[6] | Y/C[6] | C[6] | C[6] | DAT[6]
DISPx_DAT7 | DAT[7] | G[2] | G[1] | B[7] | Y/C[7] | C[7] | C[7] | DAT[7]
DISPx_DAT8 | DAT[8] | G[3] | G[2] | G[0] |  | Y[0] | C[8] | DAT[8]
DISPx_DAT9 | DAT[9] | G[4] | G[3] | G[1] |  | Y[1] | C[9] | DAT[9]
DISPx_DAT10 | DAT[10] | G[5] | G[4] | G[2] |  | Y[2] | Y[0] | DAT[10]
DISPx_DAT11 | DAT[11] | R[0] | G[5] | G[3] |  | Y[3] | Y[1] | DAT[11]
DISPx_DAT12 | DAT[12] | R[1] | R[0] | G[4] |  | Y[4] | Y[2] | DAT[12]
DISPx_DAT13 | DAT[13] | R[2] | R[1] | G[5] |  | Y[5] | Y[3] | DAT[13]
DISPx_DAT14 | DAT[14] | R[3] | R[2] | G[6] |  | Y[6] | Y[4] | DAT[14]
DISPx_DAT15 | DAT[15] | R[4] | R[3] | G[7] |  | Y[7] | Y[5] | DAT[15]
DISPx_DAT16 | DAT[16] |  | R[4] | R[0] |  |  | Y[6] | 
DISPx_DAT17 | DAT[17] |  | R[5] | R[1] |  |  | Y[7] | 
DISPx_DAT18 | DAT[18] |  |  | R[2] |  |  | Y[8] | 
DISPx_DAT19 | DAT[19] |  |  | R[3] |  |  | Y[9] | 
DISPx_DAT20 | DAT[20] |  |  | R[4] |  |  |  | 
DISPx_DAT21 | DAT[21] |  |  | R[5] |  |  |  | 
DISPx_DAT22 | DAT[22] |  |  | R[6] |  |  |  | 
DISPx_DAT23 | DAT[23] |  |  | R[7] |  |  |  | 
DIx_DISP_CLK | PixCLK |  |  |  |  |  |  | 
DIx_PIN1 |  |  |  |  |  |  |  | VSYNC_IN
DIx_PIN2 | HSYNC |  |  |  |  |  |  | 
DIx_PIN3 | VSYNC |  |  |  |  |  |  | 
DIx_PIN4 |  |  |  |  |  |  |  | 
DIx_PIN5 |  |  |  |  |  |  |  | 
DIx_PIN6 |  |  |  |  |  |  |  | 
DIx_PIN7 |  |  |  |  |  |  |  | 
DIx_PIN8 |  |  |  |  |  |  |  | 
DIx_D0_CS |  |  |  |  |  |  |  | CS0
DIx_D1_CS |  |  |  |  |  |  |  | CS1
DIx_PIN11 |  |  |  |  |  |  |  | WR
DIx_PIN12 |  |  |  |  |  |  |  | RD
DIx_PIN13 |  |  |  |  |  |  |  | RS1
DIx_PIN14 |  |  |  |  |  |  |  | RS2
DIx_PIN15 | DRDY/DV |  |  |  |  |  |  | DRDY
DIx_PIN16 |  |  |  |  |  |  |  | 
DIx_PIN17 |  |  |  |  |  |  |  | 
External Use 15

## Slide 20
IPUv3H – Video In Support
External Use 15

## Slide 21: i.MX51, i.MX53, i.MX6 D/Q – Video In Support
Feature |  | i.MX51 (IPUv3EX) | i.MX53 (IPUv3M) | i.MX6 D/Q (2 x IPUv3H)
Video Input Interfaces | Parallel | Two ports, 20 bits + 8 bits |  | 
 |  | 120 MHz; e.g. 6 MP @ 15 fps | 180 MHz; e.g. 9 MP @ 15 fps | 200 MHz; e.g. 10 MP @ 15 fps
 | MIPI/CSI-2 | No |  | One port, 4 lanes x 1 Gbps
Video Rate | Playback | 720p30 (1280x720) @ 30 fps | 1080i/p (1920x1080) @ 30 fps | 1080i/p + D1 @ 30 fps
 | Record | D1 (720x480@30 fps or 720x576@25 fps) | 720p30 (1280x720) @ 30 fps | 1080p @ 30 fps
 | 2-way |  | 720p @ 20 fps | 720p @ 30 fps
Video Processing | De-interlacing | High-quality motion adaptive algorithm |  | 
 | Resizing | Yes – fully flexible |  | 
 | Rotation/inversion | Yes |  | 
 | Color conversion | Yes – fully flexible |  | 
Memory Interface | Protocol | AXI – Including split transaction |  | 
 | Throughput | 64-bit, 133 MHz | 64-bit, 200 MHz | 64-bit, 266 MHz
Efficient memory bus utilization |  | Selective read for combining |  | 
Control capabilities |  | Display controller, DMA controller, Internal synchronization Autonomous operations: display refresh/update, view-finder |  | 
Synchronization (to prevent tearing) |  | Double/triple buffering Frame-by-frame or tight – sub-frame (utilizing internal memory) |  | 
External Use 15

## Slide 22: Video Input Ports In i.MX6 D/Q
Three ports; up to six input channels
  Two parallel – connected directly to the IPUs; independent clock and format setting
  One MIPI/CSI-2 – can transfer up to four concurrent channels
  Each port: up to 150Mpxl/s @200MHz, e.g. 10Mpxl @ 15fps
Four concurrent channels
  Each IPU has two input ports (CSI0 and CSI1), each can process an input channel from one of the external ports.
  The MIPI/CSI-2 bridge sends all its channels to all the IPU input ports and each port can select for processing a different channel, identified by its DI (Data Identifier).
  Additional channels can be transferred through a CSI transparently – as generic data – directly to the system memory.
Formats supported:
− BT.656
− BT.1120
  YUV422, RGB888, YUV444 = over an 8 bit bus
  RAW format up to 16bpp which will be translated to 8 bit using companding
  Generic data up to 20bit
MIPI/CSI-2
Receiver
i.MX6 D/Q
IPU #0
MIPI/CSI-2
Parallel 0
CSI0
CSI0
Parallel 1
mux
Video Sources
mux
IPU #1
CSI1
CSI1
External Use 15

## Slide 23: IPUv3H – The camera port
IC (Image
Converter)
IDMAC
(Image DMA
Controller)
VDI (Video De-Interlacer)
Memory
64-bit AXI
CSI (Camera
Sensor I/F)
SMFC (Sensor Multi FIFO Ctrl.)
Cameras
CSI (Camera Sensor I/F)
display
External Use 15

## Slide 24: The Camera Sensor Interface - CSI
Role: controls the camera port
  Provides direct connectivity to relevant image sensors and connectivity bridges: CSI-2, HDMI receiver, TV decoder…
Data bus – up to 20 bits
  Single value – up to 16 bits
  Two values – up to 10 bits each; e.g. HDTV YUV 4:2:2 input
Variety of data formats
  Main (with on-the-fly processing): YUV 4:2:2/4:4:4, RGB 16/24 bpp
  Other: as generic data, including compressed streams
  All primary CSI-2 formats
Frame resolution
  Up to 8192 x 4096 pixels
Input rate
  240M values/sec peak (@ 264 MHz internal clock)
Additional features
  Frame rate reduction – by skipping (reduction ratio: m:n, m<=n<=12)
  Window-of-interest selection – by cropping
External Use 15

## Slide 25: i.MX37, i.MX51, i.MX53, i.MX6 D/Q – Video in Support
How to calculate the video in pixel clock?
FW = Frame Width
FH = Frame Height
FPS = Frame rate (fps)
BI = Blanking interval
Provided in the device’s DS up to 35% (1.35).
D = Data format
How the data is arranged on the bus – (cycles/pixel)
The pixel clock [MHz] is calculated according to:
F = FW X FH X FPS X BI X D
External Use 15

## Slide 26: 16-bit camera support
16-bit YUV422
  CSI receives 2 components per cycle.
  CSI [16 bit generic data.] => SMFC => MEM [16bit generic data] => IPU[YUV422]
16-bit RGB as generic data
  CSI receives 3 components per cycle.
  Use a 16 bit sample of it (such as RGB565)
  CSI [16 bit generic data.] => SMFC => MEM [16bit generic data] => IPU [16 bit RGB] =>
IPU [map to 24bpp RGB]
16-bit RGB565
  On the fly processing of 16 bit data.
  CSI is programmed to receive 16 bit generic data.
  The interface is restricted to be in "non-gated mode" and the CSI#_DATA_SOURCE bit has
to be set
  If the external device is 24bit - the user can connect a 16 bit sample of it (RGB565 format).
  The IPU has to be configured in the same way as the case of CSI#_SENS_DATA_FORMAT=RGB565
External Use 15

## Slide 27: BT.1120/BT.656 support
BT.656
  CCIR progressive/interlaced modes
BT.1120
  CCIR progressive/ interlaced mode
  SDR/DDR mode
The timing reference signals (Sync events) are embedded in the
data.
The CCIR codes are defined in the standard. IPU can support non standard codes using the CCIR registers.
On the fly processing is supported in both modes
External Use 15

## Slide 28: BT.1120/BT.656 support
IPUv3 is an 8bit per component system.
In a 10bit data inputs there are few ways to handle the data
Companding - programmable piecewise-linear map
Regular and tight packing to memory
BT.1120 mode | connectivity | companded | regular packing | tight packing
20bit, YUV422-10 | D[19:0] | {8DC,8DC,8DC,8R} | {16DE,16DE,16DE,16R } | {10DE,10DE,10DE,2R}
20bit, YUV422-8 | D[19:12], D[9:2] | {8DC,8DC,8DC,8R} | {8D,8D,8D,8R} | NA
DC - data after being companded DE - data after being extended. R- reserved bits
External Use 15

## Slide 29: i.MX37, i.MX51, i.MX53, i.MX6 D/Q – Video in Support
Data Format | CSI Bus width | D (cycles/pixel) | comment
RGB888/YUV444 | 8 | 3 | D[19:12]
YUV422 | 8 | 2 | D[19:12]
YUV422 | 16 | 1 | D[19:4]
Generic data | 16 | 1 | D[19:4]
RGB565 | 8 | 1 | D[19:12]
RGB565 | 16 | 2 | D[19:4]
BT.1120 | 20 | 1 | D[19:0]
BT.1120 | 16 | 1 | D[19:12], D[9:2]
BT.656 | 8 | 2 | D[19:12]
Bayer | 16 | 1 | D[19:4]
F = FW X FH X FPS X BI X D
External Use 15

## Slide 30: CSI data mapping
 | RGB888/ YUV444 | RGB565 8bit | RGB565 16bit | YUV4:2:2 | Generic data | BT.656 | YUV422 16 bit | BT.1120 (YUV422-10) | BT.1120 (YUV422-8)
CSI1_D19 | D7 | D7 | R4 | D7 | MSB | D7 | Y7 | Y9 | Y7
CSI1_D18 | D6 | D6 | R3 | D6 | MSB-1 | D6 | Y6 | Y8 | Y6
CSI1_D17 | D5 | D5 | R2 | D5 | MSB-2 | D5 | Y5 | Y7 | Y5
CSI1_D16 | D4 | D4 | R1 | D4 | MSB-3 | D4 | Y4 | Y6 | Y4
CSI1_D15 | D3 | D3 | R0 | D3 | MSB-4 | D3 | Y3 | Y5 | Y3
CSI1_D14 | D2 | D2 | G5 | D2 | MSB-5 | D2 | Y2 | Y4 | Y2
CSI1_D13 | D1 | D1 | G4 | D1 | MSB-6 | D1 | Y1 | Y3 | Y1
CSI1_D12 | D0 | D0 | G3 | D0 | MSB-7 | D0 | Y0 | Y2 | Y0
CSI1_D11 |  |  | G2 |  | MSB-8 |  | CrCb7 | Y1 | 0
CSI1_D10 |  |  | G1 |  | MSB-9 |  | CrCb6 | Y0 | 0
CSI1_D9 |  |  | G0 |  | MSB-10 |  | CrCb5 | CrCb9 | CrCb7
CSI1_D8 |  |  | B4 |  | MSB-11 |  | CrCb4 | CrCb8 | CrCb6
CSI1_D7 |  |  | B3 |  | MSB-12 |  | CrCb3 | CrCb7 | CrCb5
CSI1_D6 |  |  | B2 |  | MSB-13 |  | CrCb2 | CrCb6 | CrCb4
CSI1_D5 |  |  | B1 |  | MSB-14 |  | CrCb1 | CrCb5 | CrCb3
CSI1_D4 |  |  | B0 |  | MSB-15 |  | CrCb0 | CrCb4 | CrCb2
CSI1_D3 |  |  |  |  |  |  |  | CrCb3 | CrCb1
CSI1_D2 |  |  |  |  |  |  |  | CrCb2 | CrCb0
CSI1_D1 |  |  |  |  |  |  |  | CrCb1 | 0
CSI1_D0 |  |  |  |  |  |  |  | CrCb0 | 0
External Use 15

## Slide 31
IPUv3H – Fundamentals
External Use 15

## Slide 32: The Image Processing Unit
Functions: comprehensive support for the flow of data from an image sensor and/or to a display device.
  Connectivity to relevant devices
  Related image processing and manipulation
  Synchronization and control capabilities
Memory Interface
Sync & Control
Camera Interface
Display Interface
Memory
IPU
Video Sources
Displays
Optional Interface Bridges
MCU
Processing
Including Image Enhancements And Conversions
External Use 15

## Slide 33: IPUv3H – Internal Structure
TM
IC (Image Converter)
IDMAC
(Image DMA
Controller)
DC
(Display Contr.)
IPUv3H
Memory
IRT (Image Rotator)
DP (Display Processor)
CM (Control Module)
32-bit AHB
MCU
64-bit AXI
CSI (Camera Sensor I/F)
DI
(Display I/F)
DMFC (Display Multi FIFO Ctrl.)
SMFC (Sensor Multi FIFO Ctrl.)
Cameras
Displays
VDI (Video De-Interlacer)
External Use 33

## Slide 34: IPUv3 Fundamentals - The display port
The display port handles all the IPUv3 features targeted for controlling and sending data to the display.
The display port consists of 4 modules:
DC - a display controller
DP - a display processor
DMFC - a display multi-FIFO controller
DI - a display interface. The DI is instantiated twice to provide two symmetrical display interfaces.

## Slide 35: IPUv3 Fundamentals - Supported display interfaces
The total number of supported displays by IPUv3 is 4.
The display port has 2 DI interfaces.
Each interface can handle up to 3 displays.
Each DI can handle up to 2 asynchronous interfaces (e.g. Smart LCD, Graphic accelerator) - only one of them can be serial interface.
Each DI can handle one synchronous interface (e.g. TV, dumb LCD).

## Slide 36: IPUv3 Fundamentals – display channels’ mapping
The display port supports multiple flows that may have different characteristics
In order to configure the IPU we need to identify some of the flow’s characteristics and allocate the IPUv3’s resources that will participate in that flow.
First we need to understand how the channels are distributed.

## Slide 37: IPUv3 Fundamentals – display channels’ mapping
Ch # | Destination | DMFC/DC numbering | Flow’s nature | Alpha channel | comment
21 | DC |  | SYNC or ASYNC | NA | Direct flow via IC. If this flow is used it replaces once of the DMFC channels.
23 | DP - primary | 5B/5 | SYNC | 51 | Ch 23 is associated with ch27. when there’s only one plane in the flow – this channel should be used.
24 | DP - Primary | 6B/6 | ASYNC | 52 | Ch 24 is associated with ch29. 2 ASYNC flows can use this channel via alternate flow. when there’s only one plane in the flow – this channel should be used.
27 | DP -Secondary | 5F/5 | SYNC | 31 | 
28 | DC | 1/1 | SYNC or ASYNC | NA | if ch28 is connected to DI0 then ch23 must be connected to DI1
29 | DP -Secondary | 6F/6 | ASYNC | 33 | 

## Slide 38: IPUv3 Fundamentals – display channels’ mapping
Ch # | Destination | DMFC/DC numberin g | Flow’s nature | Alpha channel | comment
40 | DC | 0/0 | Read | NA | 
41 | DC | 2/2 | ASYNC | NA | 
42 | DC | 1C | Command | NA | Refer to the spec for the command channel restrictions
43 | DC | 2C | Command | NA | Refer to the spec for the command channel restrictions
44 | DC | 3 | Mask | NA | Mask channel can be associated with ch 23 or ch 28

## Slide 39: IPUv3 Fundamentals - DI
The DI is responsible for the timing waveforms of each signal in the display’s interface.
The DI is composed of
  8 sets of waveform generators controlling signals associated with the DI’s clock; These signals drive PIN1-PIN8. These pins can be used for signals like VSYNC,HSYNC
  12 sets of waveform generators controlling signals associated with the data; These signals drive PIN11-PIN17 + 2 CS signals.
These pins can be used for signals like DRDY,CS,RS
  The DI generates the clock to the display
    The DI clock can be derived from the IPUv3 hsp_clk
    The DI clock can be derived from an external to the IPU clock (PLL or pin)

## Slide 40
IPUv3 Fundamentals - DI
This waveform describe how the display clock’s parameters are set.

## Slide 41
IPUv3 Fundamentals - DI
This waveform describe how the DI’s PIN parameters are set.

## Slide 42
IPUv3 Fundamentals - DI
This waveform provides an example of waveform concatenation.

## Slide 43: IPUv3 Fundamentals - DC
The DC (Display Controller) is responsible for:
Activation of a flow
  When there’s new content to be displayed (asynchronous flow)
  Upon an internal timer (synchronous flow)
Linkage between the microcode to
  mapping units (within DC)
  and timing units (within DI)

## Slide 44: 3 Fundamentals -
IPUv
DC
uCODE
Routine
uCODE
Routine
uCODE
Routine
(
Mapping
unit
DATA handling)
(
Mapping
unit
DATA handling)
Mapping Unit (DC)
(DATA handling)
D
I’s Waveform generators
(timing characteristics)
D
I’s Waveform generators
(timing characteristics)
DI’s Waveform generators
(timing characteristics)
Events
(NL, NF, New Data…)

## Slide 45: IPUv3 Fundamentals - DMFC
The DMFC is a multi FIFO controller utilizing a single memory to serve the DC and DP channels.
The FIFO is partitioned to 8 equal segments. The segments can be allocated asymmetrically to the channels.
The memory allocation for a specific channel must not be greater than a certain number of rows. The exact number is different from one channel to another (see the spec).
When the direct path from the IC is used, this channel replaces one of the existing DMFC channels.

## Slide 46: The Image DMA Controller – IDMAC
Role: control the memory ports; transfer data to/from system memory
Memory ports - AXI
  IMDAC: 1 read, 1 write
Throughput:
  External: 64 bits @ 264 MHz
  Internal: up to 2 pixels/cycle @ 264 MHz (through each port)
  Shared by all DMA channels: input from sensor, output to display and off-line processing
-> efficient utilization of the bandwidth in different use cases
  Efficient pipelining: 4 AXI ID’s; multiple outstanding transactions: read – 8; write – 6
Data arrangement in memory
  Row-after-row, with flexible line-stride – as needed for a window in a video/graphics buffer
Access order
  Block-by-block – for rotation
  Row-by-row – used for all other channels
    Needed for output to display or input from sensor
    Decreases the memory bus load by increasing its utilization efficiency

## Slide 47: The Image DMA Controller – IDMAC (cont.)
A variety of pixel formats
− YUV 4:2:0/4:2:2/4:4:4 – for video
  Conventionally packed RGB pixels – 8/16/32 bpp – for graphics
  Tightly packed RGB pixels – 12/18/24 bpp
    For reduced load on the memory bus and for power-efficient screen refresh
  Optional independent alpha (translucency) input
    For planes that do not have interleaved alpha
  Coded color (using a LUT; 4/8 bpp)
    An additional option to reduce bus load and power
  Gray scale
  Generic data
Additional features
  Conditional read (for combining) – transparent pixels are not read
    Pixel transparency – identified from the independent alpha input
  Scrolling and panning
  Uniform programming model for all channels
  (stored in the CPMEM – channel parameter memory)

## Slide 48: IPUv3 Fundamentals - IDMAC
The IDMAC of IPUv3 is connected to the AXI bus.
  Full separation between read and write
  All the channels are symmetric
  64-bit AXI bus, internal bus of 128-bit (4 pixels)
Each channel uses 2X160 words of the CPMEM memory, holding
the channels settings
Ability to use alternate rows in the CPMEM for alternate flows
Usage of alpha located in separate buffers (ATC)
Dynamic and static arbitration between channels.
Prioritizing screen refresh channels over other IPU channels and other DDR masters

## Slide 49: DP (Display Processor)
DP has following features;
  Support input format YUVA/RGBA
  Combining 2 video/graphics planes
  Color conversion (YUV <-> RGB, YUV<->YUV) & Correction (gamut- mapping)
  Gamma correction and Contrast stretching
  Support output format YUV/RGB
  Dynamic task switching between async and sync flows
Color Conversion & Correction
DP
Color Conversion & Correction
Color
Co on
Correct
nversi
& ion
Gamma Correction & Contrast Stretching
4x3x8 bits
Alternative
Locations
Output FIFO
To DC
From DMFC
4x4x8 bits
Cursor Overlay
Combining
Primary Secondary
Additional Plane
Main Plane (full screen)
Input FIFO
Input FIFO
Primary Secondary

## Slide 50: IPUv3 Fundamentals - DP
The DP handles the content of the frame.
It performs image processing on the way to the display (combining, CSC, gamma correction)
The DP supports one synchronous flow and two asynchronous flows.
All the DP configuration is done only via the SRM. The control module handles the automatic switch between DP settings when the DP switches from one flow to another.

## Slide 51: IC (Image Converter)
Resizing
  Fully flexible resizing ratio
Maximal downsizing ratio: 8:1 Maximal upsizing ratio: 1:8192
  Independent horizontal and vertical resizing ratios
Color conversion/correction
− YUV <-> RGB, YUV <-> YUV conversion
Combining with a graphic plane
Max output width 1024 pixels. Larger images are processed in stripes
IC
Video Input FIFOs
Down-Sizing Row Buffers
Power-Of-Two Down-Sizing
Horizontal Bilinear Resizing
Resizing Row Buffers
Vertical Bilinear Resizing
Color Conversion & Correction
Combining
Graphics Input FIFOs
Output FIFOs
To IDMAC/DMFC
From IDMAC
From IDMAC
Color Conversion & Correction

## Slide 52: The Image Rotator - IRT
Role: performs rotation and inversion
− Rotation: 90, 180, 270
degrees
  Inversion: horizontal and vertical
Rate: up to 100M pixels/sec
  (depends on use case)
Additional features
  Acts on 8x8 blocks
  Multi-tasking: up to three tightly time-shared tasks – block-by-block
  Pixel format: 24-bit

## Slide 53: The Video De-Interlacer or combiner - VDIC
Role 1: performs de-interlacing – converting interlaced video to progressive
Method: a high-quality motion adaptive filter
  For slow motion – retains the full resolution (of both top and bottom fields), by using temporal interpolation
  For fast motion – prevents motion artifacts, by using vertical interpolation
Resolution: field size up to 968x1024 for i.MX6 and 720x1024 in i.MX5 pixels. Larger
frames are processed in stripes (split mode).
Output rate: up to 120M pixels/sec
Additional features
  Uses three input fields for each output frame
(the minimum needed for a reliable motion detection)
  Vertical interpolation – 4-tap filter; using an internal row buffer
  Single concurrent flow
  Input may come from a video decoder (VPU) or directly from the CSI

## Slide 54: The Video De-Interlacer or combiner - VDIC
Role 2 : performs combining – overlaying of 2 frames at the same color space
As an alternative to the de interlacing function the VDIC HW can perform combining
  Combining of 2 planes
  Doesn’t have to be of the same size
  Must be of the same color space (no CSC)
  Perform 1 pixel per cycle
  Color keying, alpha blending

## Slide 55
IPUv3H – Combining

## Slide 56: IPUv3 – Basic Combining Capabilities
Combining methods (in both cases)
  Color keying and/or alpha blending
  Alpha: global or per-pixel; interleaved with the pixels (upper plane) or as a separate input
i.MX37/51/53/6 Dual/Quad | 
DI DP DC DI IPUv3 IC | 
External Memory
Plane 1
Plane 2
Plane 3
Plane 4
Combining in the Display Processor (DP)
Two planes
One plane may have any size and location
The other one must be “full-screen” (cover the full output area)
Maximal rate: i.MX37/51 – 133 MP/sec, i.MX53 – 200 MP/sec, i.MX6 Dual/Quad – 264 MP/sec
Combining in the Image Converter (IC)
Two planes; both “full-screen” (cover the full output area)
Maximal rate: i.MX37/51 – 20 MP/sec , i.MX53 – 30 MP/sec, i.MX6 Dual/Quad – 40 MP/sec
Note: This is the capability per IPUs, so the total capability of the processor is doubled in i.MX6DQ.

## Slide 57: IPUv3 – Off-Line Combining
Unlimited number of planes combined sequentially
External Memory
i.MX37/51/53/6 Dual/Quad
VDIC
Or IC
IPUv3
Temporary
Top plane
VDIC Or IC
Temporary
Plane 3
VDIC Or IC
Plane 1 (bottom)
Plane 2
Result
Same HW
Combining in the VDIC (Video De-Interlacer & Combiner) – i.MX53/6 Dual/Quad only
Available when de-interlacing is not needed
Two planes; each may have any size and location (supplemented by a “background color”)
Maximal rate: i.MX53 – 180 MP/sec, i.MX6 Dual/Quad – 240 MP/sec
Combining method – as in the DP and IC
Note: This is the capability per IPUs, so the total capability of the processor is doubled in i.MX6DQ.

## Slide 58: IPUv3 – Maximal On-The-Fly Combining To A Single Display
3-planes i.MX37/51 – up to 20 MP/sec
Note: the bottom plane may be a result of additional off- line combining of several planes
External Memory
i.MX37/51
IC
IPUv3
Plane 3 (top)
DC
DI
DP
Plane 1 (bottom)
Plane 2
External Memory
i.MX53/6 Dual/Quad
IC
IPUv3
Plane 4 (top)
DC
DI
DP
Plane 3
4-planes
i.MX53 – up to 30 MP/sec i.MX6 Dual/Quad – up to 40 MP/sec
VDIC
Plane 1 (bottom)
Plane 2
Note: This is the capability per IPUs, so the total capability of the processor is doubled in i.MX6DQ.

## Slide 59: i.MX6 Dual/Quad: On-The-Fly Combining Using 2x IPUv3
i.MX6 Dual/Quad
Note: Some planes may be a result of additional off-line combining of several planes. Such combining may be performed either with IPUs or GPUs.
IC
IPUv3 - 1
External Memory
Plane 8 (top)
DC
DI
DP
Plane 7
VDIC
Plane 5 (bottom)
Plane 6
External Memory
i.MX6 Dual/Quad
IC
IPUv3 - 0
Plane 4 (top)
DC
DI
DP
Plane 3
VDIC
Plane 2
i.MX6 Dual/Quad
IC
IPUv3 - 1
External
Memory
Plane 7 (top)
DC
DI
DP
Plane 6
VDIC
Plane 5
i.MX6 Dual/Quad
IC
IPUv3 - 0
External
Memory
Plane 4
DC
DI
DP
Plane 3
VDIC
Plane 1 (bottom) Plane 1 (bottom)
Plane 2
CSI
Example 1: 2x 4 planes
Example 2: 1x 7 planes
i.MX6 Dual/Quad
IC
IPUv3 - 1
Plane 7
External
Memory
Plane 8
DC
DI
DP
DI
Plane 5 (bottom)
Plane 6
i.MX6 Dual/Quad
IC
IPUv3 - 0
Plane 3
External Memory
Plane 4
DC
DI
DP
DI
Plane 1 (bottom)
Plane 2
Example 3: 4x 2 planes

## Slide 60: IPUv3 combining capabilities – summary
*The output of the IC can be sent directly to a smart display
60
 | DP | IC | VDIC
Output | Display | Memory* | Memory
Relations between planes | PlaneA <= PlaneB | PlaneA = PlaneB | PlaneA <= PlaneB
Color space conversion | Yes | Yes | No
Performance | 1 cycle/pixel | 4 cycle/pixel | 1 cycle/pixel
HW cursor | 32x32 unified color | No | No
Output Image size | FW up to 2048 | FW up to 1024 | FW up to 1920
Color keying | Yes |  | 
Alpha blending | Yes |  | 

## Slide 61: IPUv3 Fundamentals – programming steps
This is a high level example of IPUv3 programming flow.
What are the displays connected in the use case?
  Allocated the displays to each DI
  Define the timing characteristics of each signal for each display.
Define each flow in the DC
  sync/async
  Define the events that trigger the flow – and what to do upon their arrival
  Allocate mapping unit, and mapping scheme
  Allocate waveform generator in the DI
Configure the DP for each flow
Configure the IDMAC
  How the data is arranged in the memory (interleaved/not interleaved)
  What’s the data’s format (PFS, BPP) , mapping
Processing: VDIC, IC (Resizing, CSC) and rotation settings
Control module configuration for activation of a flow
  Define the trigger to start a flow
  Define is the processing chain

## Slide 62
IPUv3H – Control

## Slide 63: The control Module - CM
The control module is responsible for the flow management within the IPU.
The module is composed of
  General control Registers (GCR)
  Frame synchronization unit (FSU)
  Shadow registers module (SRM)
  Interrupt controller
  Low Power modes controller
  Debug unit

## Slide 64
FSU – double buffering
Similar to IPUv1 the data is tightly pipelined using double buffering

## Slide 65: FSU – task chaining
65

## Slide 66
Peripherals

## Slide 67: MIPI DSI
Features of the MIPI DSI complex: Supported standard version:
MIPI DSI Compliant
DSI Version 1.01
DPI Version 2.0
DBI Version 2.0
DSC Version 1.02
PPI for D-PHY
MIPI D-PHY Version 1.0
Configuration: one clock lane, two data lanes
Speed: Up to 1Gb/s per lane (fast speed). Low speed/low power signaling supported
DSI can support both command and video modes and up to four virtual channels to accommodate multiple displays.
Command and video mode support (type 1, 2, 3, and 4 display architecture)
Mode switching: low power and ultra low power
Burst mode/Non-burst mode
Bus turnaround
Fault error recovery scheme
Both DPI and DBI coexist in the system but only one of them could be active in a certain time
The DSI MIPI Interface is a digital core accompanied with a multi-lane D-PHY that implements all protocol functions defined in the MIPI DSI Specification, providing an interface between the System and MIPI DSI compliant Display

## Slide 68: MIPI CSI-2
The features of the MIPI CSI-2 complex:
Supported standard version: MIPI CSI-2 Version 1.0
Configuration: one clock lane, four data lanes
Speed: Up to 1Gb/s per lane
Throughput: 250MB/sec
Timing accurate signaling of Frame and Line synchronization packets;
Support for several frame formats such
as:
  General Frame or Digital Interlaced Video with or without accurate sync timing
  Data type (Packet or Frame level) and Virtual Channel interleaving
32-bit Image Data Interface delivering data formatted as recommended in CSI-2 Specification;
  Directly supports all primary data formats conversion to IPU input. Some secondary formats are treated as “generic” data
  RGB, YUV and RAW color space definitions;
  From 24-bit down to 6-bit per pixel;
  Generic or user-defined byte-based data types
The CSI-2 MIPI Interface is a digital core accompanied with multi-lane D-PHY that implements all protocol functions defined in the MIPI CSI-2 Specification, providing an interface between the System and MIPI CSI-2 compliant Camera Sensor

## Slide 69: LVDS Interface in i.MX53 & i.MX6 D/Q – Key Features
Structure
  Two Channels
  Each channel contains 4 data pairs + 1 clock pair
Data
  18 bpp pixels – using 3 LVDS data pairs
  24 bpp pixels – using 4 LVDS data pairs
Control signals: HSYNC, VSYNC, DE
Pixel clock rate
  Single Channel: up to 85 MHz; e.g. WXGA @ 60 fps or 720p60
  Dual Channel: up to 170 MHz; e.g. UXGA @ 60 Hz or 1080p60
Relevant Standards
  PHY Standard: ANSI EIA-644A
  Display Protocol Standards:
    SPWG Standard Panel Working Group Specification 3.8 (May 2007)
    VESA PSWG – Panel Standardization Working Group – set of standards for panels using LVDS.
    JEIDA/JEITA DISM Standard JEIDA-59-1999
    OpenLDI (National) – Revision 0.95 13/May/1999. *Only* Unbalanced operating mode supported (aligned with vast majority of LCD vendors).

## Slide 70: LVDS – what is supported?
Single Channel configuration
  Pixel clock: up to 85 MHz; e.g. WXGA @ 60 fps or 720p60
  LVDS Clock frequency = Pixel clock x 7 = 85*7 = 595Mhz
  Data :
    18 bpp pixels – using 3 LVDS data pairs
    24 bpp pixels – using 4 LVDS data pairs
Dual Channel configuration
  Pixel clock: up to 170 MHz; e.g. UXGA @ 60 Hz or 1080p60
  LVDS Clock frequency = Pixel clock x 7/2 = 170*7/2 = 595Mhz
  Data :
    18 bpp pixels – using 3 LVDS data pairs per channel
    24 bpp pixels – using 4 LVDS data pairs per channel

## Slide 71: LDB Features
LDB Structure:
  2 Channels , same/independent data
  Each channel contains 4 data pairs + 1 clock pair
Resolutions/Rates:
  Single Channel (up to WXGA): Up to 85 MHz, 3 or 4 data pairs
  Dual Channel (up to UXGA): Up to 170 MHz, 6 or 8 data pairs
  For example: can support 1080p60 or UXGA @60fps
Pixel Depths:
  18 bpp – 3 LVDS data pairs
  24 bpp – 4 LVDS data pairs
Control signals:
  Supports HSYNC, VSYNC, DE

## Slide 72: HDMI General Features
Description: High-Definition Multimedia Interface (HDMI) Transmitter including both HDMI TX Controller and PHY
Standard Compliance: HDMI 1.4a, DVI 1.0, HDCP 1.4 (with keys stored in embedded eFuses)
− Supporting majority of primary 3D Video formats
TMDS Core Frequency: From 25 MHz to 340 MHz
Consumer Electronic Control: Supported
Monitor Detection: Hot plug/unplug detection and link status monitor support
Testing Capabilities: Integrated test module
Maximal Power Consumption: 70mW
Temperature Range: -40C to +125C (Tj)

## Slide 73: i.MX6 Dual/Quad: HDMI Video/Audio Features
Video Standard Compliance: EIA/CEA-861D
Supported Video Resolutions: Up to 1080p@60Hz and 720p/1080i@120Hz HDTV display; up to QXGA graphics display
Pixel Clock Frequency: From 25 MHz to 240 MHz
Video Data Formats: YCbCr 4:4:4; RGB 4:4:4; YCbCr 4:2:2
Internal Video Processing: Interpolation YCbCr 4:2:2 to 4:4:4;
conversion YCbCr to RGB and vice versa
Audio Standard Compliance: IEC60958, IEC61937
Supported Audio Formats: All audio formats as specified by the
HDMI Specification Version 1.4a
Audio Input Interfaces: Embedded Audio DMA
Audio Sampling Rate: Up to 192 kHz

## Slide 74
IPU & the iMX Linux BSP

## Slide 75: IPU Drivers
IPU drivers are based on code re-used from MX5x IPU driver
  Key modification: Support for multiple instances provides support for the 2
IPU modules in i.MX 6Quad/Dual
IPU functionality accessed through multiple interfaces:
  IPU framebuffer (FB) driver: Accessed through the Linux standard FB interface
    Introduction of MXC Display Driver framework, to manage interaction between IPU and display device drivers (e.g., LCD, LVDS, HDMI, MIPI, etc.)
  IPU processing driver: A custom API exposes IPU processing functionality
    Resizing
    Rotation
    Combining of graphics planes
    CSC
    De-interlacing
  Video 4 Linux 2 (V4L2) output driver: Based on V4L2 video API, leverages IPU
processing driver
  V4L2 capture driver: Based on V4L2 capture API; leverages IPU processing driver and IPU core driver

## Slide 76: IPU Drivers
Architecture Design:
  IPU sub-module (CSI, IC, DI, DP, IDMAC, etc) functionality provided in a set of IPU Core driver functions
    Largely unmodified between MX5x and MX 6Quad
  Leverage existing Linux APIs:
    For framebuffer access (IPU FB driver)
    Video image processing and display (V4L2 output driver)
    Image capture (V4L2 capture driver)
  Fill in gaps with custom APIs and API extensions:
    Extensions to FB interface to control certain IPU functionality – local and global alpha, gamma correction, etc.
    IPU Processing driver to provide user space access to IPU processing capabilities
  Provide MXC Display Driver (mxc_dispdrv.h) framework to simplify connection between display devices and IPU modules.

## Slide 77: IPU Drivers
IPU Core Driver (CSI/IDMA/IC/DC/DP)
V4L2 Soc-Camera Subsystem |  | 
Cameras |  | mxc v4l2 capture
V4L2 Video Framework | 
 | mxc v4l2 output
IPU Processing Driver
MXC Display Driver Framework
Display Device Drivers
(LCD, LVDS,
HDMI, etc)
User space
Hardware
Frame Buffer Core |  | 
 | IPU FB driver | 
Kernel Core Software Freescale BSP Software Hardware

## Slide 78: Overview of IPU Drivers
• MXC Display Driver
− Simple framework to manage MXC display device drivers.
− Examples: LCD, TVE, MIPI, VGA, HDMI
IPU Processing Driver
  Manage IPU IC tasks in kernel space.
MXC V4L2 Drivers
  Based on IPU processing driver.

## Slide 79: MXC Display Driver - Files
MXC Display Driver files drivers/video/mxc/mxc_dispdrv.h drivers/video/mxc/mxc_dispdrv.c
IPU framebuffer driver drivers/video/mxc/mxc_ipuv3_fb.c
Display device drivers drivers/video/mxc/mxc_lcdif.c drivers/video/mxc/mxc_hdmi.c drivers/video/mxc/mipi_dsi.c
…

## Slide 80: MXC Display Driver - Structures
struct mxc_dispdrv_driver { const char *name;
int (*init) (struct mxc_dispdrv_handle *, struct mxc_dispdrv_setting *); void (*deinit) (struct mxc_dispdrv_handle *);
/* display driver enable function for extension */
int (*enable) (struct mxc_dispdrv_handle *, struct fb_info *);
/* display driver disable function, called at early part of fb_blank */ void (*disable) (struct mxc_dispdrv_handle *, struct fb_info *);
/* display driver setup function, called at early part of fb_set_par */ int (*setup) (struct mxc_dispdrv_handle *, struct fb_info *fbi);
};
struct mxc_dispdrv_setting {
/*input-feedback parameter*/ struct fb_info *fbi;
int if_fmt;
int default_bpp; char *dft_mode_str;
/*feedback parameter*/ int dev_id;
int disp_id;
};

## Slide 81: MXC Display Driver - Functions
struct mxc_dispdrv_entry *mxc_dispdrv_register(
struct mxc_dispdrv_driver *drv);
int mxc_dispdrv_unregister(struct mxc_dispdrv_entry *entry); struct mxc_dispdrv_handle *mxc_dispdrv_gethandle(char *name,
struct mxc_dispdrv_setting *setting);
int mxc_dispdrv_setdata(struct mxc_dispdrv_entry *entry, void *data);
void *mxc_dispdrv_getdata(struct mxc_dispdrv_entry *entry);

## Slide 82: MXC Display Driver – Configuration Flow
LDB
RGB666 LDB-XGA
Ipu0
di1
mxc_dispdrv List
IPUv3 fb driver dev=ldb mode_str=? fbi
1
2
3
mxc_dispdrv_register mxc_dispdrv_setdata
mxc_dispdrv_gethandle
init
4
fb_add_videomode fb_set_var

## Slide 83: MXC Display Driver
Command Line Options: first display:
video=mxcfb0:dev=dispdrv_name,mode_str,if=if_fmt
second display:
video=mxcfb1:dev=dispdrv_name,mode_str,if=if_fmt
For example: video=mxcfb0:dev=hdmi,1920x1080M@60,if=RGB24 video=mxcfb1:dev=ldb,LDB-XGA,if=RGB666 video=mxcfb2:dev=lcd,800x480M@55,if=RGB565

## Slide 84: MXC Display Driver – Multi-Display Options
hdmi + lvds video=mxcfb0:dev=hdmi,1920x1080M@60,if=RGB24 video=mxcfb1:dev=ldb,LDB-XGA,if=RGB666
lvds + lvds
video=mxcfb0:dev=ldb,LDB-XGA,if=RGB666 video=mxcfb1:dev=ldb,LDB-XGA,if=RGB666
lcd + lvds video=mxcfb0:dev=lcd,800x480M@55,if=RGB565 video=mxcfb1:dev=ldb,LDB-XGA,if=RGB666
hdmi + lvds + lvds video=mxcfb0:dev=hdmi,1920x1080M@60,if=RGB24 video=mxcfb1:dev=ldb,LDB-XGA,if=RGB666 video=mxcfb2:dev=ldb,LDB-XGA,if=RGB666

## Slide 85: Example of MXC Display Driver - HDMI
Software Architecture:
  HDMI multifunction driver (MFD) manages software resources common to video and audio drivers
  Audio driver uses ALSA/SoC audio framework.
  Video driver:
    MXC Display Driver API to register with IPU FB driver
    Linux Framebuffer (FB) API to change the video mode and receive notifications
of mode changes

## Slide 86: I and the i.MX 6Quad Framebuffer and Display Device Architecture
HDM

## Slide 87: Overview of IPU Drivers
MXC Display Driver
  Simple framework to manage MXC display device drivers.
  Examples: LCD, TVE, MIPI, VGA, HDMI
IPU Processing Driver
− Manage IPU IC tasks in kernel space.
MXC V4L2 Drivers
− Based on IPU processing driver.

## Slide 88: IPU Processing Driver - Introduction
Each IPU has two kernel threads for IC task PP&VF
Each kernel thread performs the tasks on its task queue list
Each task executes the following sequence:
ipu_init_channel → ipu_init_channel_buffer → request_ipu_irq → ipu_enable_channel → wait_irq (task finish) → ipu_disable_channel → ipu_uninit_channel
Tasks are based on single buffer mode
Split mode tasks will be split into 2 tasks per IPU.
An application only needs to prepare a task and queue it
Task operations include
  Setting the task input/overlay/output/rotation/deinterlacing/buffer
  Call ioctl IPU_CHECK_TASK first to adjust parameters according to
feedback
  Call ioctl IPU_QUEUE_TASK to queue task
IPU_QUEUE_TASK is a blocking ioctl.

## Slide 89: IPU Processing Driver
Files
include/linux/ipu.h
drivers/mxc/ipu3/ipu_device.c
Structures
see include/linux/ipu.h
Ioctls |  | 
#define | IPU_CHECK_TASK | _IOWR('I', 0x1, struct ipu_task)
#define | IPU_QUEUE_TASK | _IOW('I', 0x2, struct ipu_task)
#define | IPU_ALLOC | _IOWR('I', 0x3, int)
#define | IPU_FREE | _IOW('I', 0x4, int)

## Slide 90: IPU Processing Driver
Example
linux-test/test/mxc_ipudev_test/mxc_ipudev_test.c

## Slide 91: IPU Processing Driver
Advantages
  Easy to use.
  Provides workaround for IPU suspend/resume issue
    Cannot suspend when double buffering is enabled
  All IC tasks may be based on this IPU processing driver, including
  user applications and V4L2 output and capture drivers
    Reason: Easier to debug if there is an issue.
Disadvantages
  Based on kernel thread, all control is done by software, so Linux scheduler may have undesirable impact on the system.
  Single-buffer mode doesn’t perform as well as double-buffer mode

## Slide 92: Overview of IPU Drivers
MXC Display Driver
  Simple framework to manage MXC display device drivers.
  Examples: LCD, TVE, MIPI, VGA, HDMI
IPU Processing Driver
  Manage IPU IC tasks in kernel space.
• MXC V4L2 Drivers
− Based on IPU processing driver.

## Slide 93: V4L2 – Common Kernel API
What is Video4Linux (V4L)?
  V4L is the original video capture/overlay API of the Linux kernel. It appeared late the 2.1.x development cycle in the Linux kernel.
What about V4L2?
  V4L2 is the second generation of the video4linux API which fixes a number of design bugs of the first version. It was integrated into the standard kernel in 2.5.x.
  V4L2 is an interface for analog radio, video capture and output drivers.
  Hardware acceleration capabilities (IPUv3) are leveraged in V4L2 drivers and provided in the Linux BSP
  Upper level software that uses the V4L2 API, such as G-streamer source/sink and Android
camera HAL, does not need to understand the underlying hardware.
Documentation / Web Resource / API spec
  Documentation/video4linux/ subdirectory in kernel tree.
  http://v4l2spec.bytesex.org - the spec of V4L2
  http://www.linuxtv.org/wiki/index.php/Main_Page - wiki for V4L and DVB

## Slide 94: MXC V4L2 – User APIs
VIDIOC_QUERYCAP
VIDIOC_G_FMT / VIDIOC_S_FMT
VIDIOC_REQBUFS
VIDIOC_QUERYBUF
VIDIOC_QBUF / VIDIOC_DQBUF
VIDIOC_STREAMON / VIDIOC_STREAMOFF
VIDIOC_G_CTRL / VIDIOC_S_CTRL
VIDIOC_CROPCAP / VIDIOC_G_CROP / VIDIOC_S_CROP
VIDIOC_ENUMOUTPUT / VIDIOC_G_OUTPUT / VIDIOC_S_OUTPUT
APIs used only for MXC V4L2 capture:
VIDIOC_ENUMINPUT / VIDIOC_G_INPUT / VIDIOC_S_INPUT
APIs used only for MXC V4L2 TV-in:
VIDIOC_ENUMSTD / VIDIOC_G_STD / VIDIOC_S_STD

## Slide 95: MXC V4L2 – Internal APIs
New version of V4L2 framework supports master / slave device drivers:
Support multiple master devices and multiple slave devices
mxc_v4l2_capture driver is the V4L2 master driver
Camera drivers and tv-in driver are V4L2 internal slave drivers
These ioctls are used in kernel internally for MXC V4L2 capture/tvin especially:
ioctl_dev_init / ioctl_dev_exit
ioctl_s_power
ioctl_g_ifparm
ioctl_init
ioctl_g_fmt_cap
ioctl_g_parm / ioctl_s_parm
ioctl_queryctrl / ioctl_g_ctrl / ioctl_s_ctrl

## Slide 96: V4L2 – Usage and Examples
How to use V4L2:
Generally, programming a V4L2 device consists of these steps:
  Opening the device
  Changing device properties, selecting a video and audio input, video standard, picture brightness, etc.
  Negotiating a data format
  Negotiating an input/output method
  Executing the actual input/output loop
  Closing the device
Please refer to the following examples:
  BSP team’s test cases:
git clone git://sw-git01-tx30.am.freescale.net/linux-test.git
(without password)
  Test team’s VTE test cases
  Camera HAL in Android source code
  G-streamer source/sink source code

## Slide 97: Features of MXC V4L2 Capture
Still capture: capture a frame in a buffer, users can read the buffer and store the picture in a file.
Preview: show the capture frames directly onto the framebuffer. Users
can choose the framebuffer number on which the video will be shown.
Video capture: capture frames in allocated buffers. Users can get the frames by calling VIDIOC_DQBUF and then send them to VPU for encoding or save them in a file.

## Slide 98: Features of MXC V4L2 Capture
To capture a still image
No resizing/rotation/CSC can be done.
− One image can be converted to be in a different pixel format within the same color space with the raw data by using CSI->SMFC->MEM IDMAC channel.

## Slide 99: Features of MXC V4L2 Capture
To preview a captured video on frame buffer
  Preview on fb0 – Resizing/rotation/CSC can be done in IC(PRP_VF) channels. Manually control the buffer ready flags in interrupt handler. Use DP(DP_BG) channel to display the captured frames.
  Preview on fb2 - Resizing/rotation can be done in IC(PRP_VF) channels. CSC can be done in DP(DP_FG) channel. The flow is totally controlled by FSU.

## Slide 100: Features of MXC V4L2 Capture
To capture frames in allocated buffers (using IC channel)
Resizing/rotation/CSC can be done in IC(PRP_ENC) channels. Manually control the buffer ready flags in interrupt handler.
MXC V4L2 capture maintains the numbers of buffers.
Users can get the captured buffer by calling VIDIOC_DQBUF ioctl and return the buffer to the kernel by calling VIDIOC_DQBUF ioctl .
NOTE: Camera preview and capturing frames into buffers can be used at the same time.

## Slide 101: Features of MXC V4L2 Capture
To capture frames in allocated buffers (using SMFC channel)
No resizing/rotation/CSC can be done. Manually control the buffer ready flags in interrupt handler.
MXC V4L2 capture maintains numbers of buffers.
Users can get the captured buffer by calling VIDIOC_QBUF ioctrl and return the buffer to the kernel by calling VIDIOC_QBUF ioctrl.

## Slide 102: Features of MXC V4L2 Output
Support for playing video using one framebuffer at a time:
  DP-BG framebuffer
  DP-FG framebuffer
  DC framebuffer
Support for the following modes:
  IC normal mode – resizing / CSC / rotation, using PP channel
  IC bypass mode – CSC, using DP or DC channel directly
  IC horizontal/vertical split mode – resizing / CSC / rotation, support high resolution output, using PP channel
  VDI-IC video deinterlacing mode - deinterlacing / resizing / CSC / rotation, using PRP_VF channel, including high motion mode and low motion mode.
Note: V4L2 output and V4L2 capture can run at the same time if there is no IC or DP/DC channel conflict.

## Slide 103: Features of MXC V4L2 Output
IC normal mode (using PP channel)
Resizing/rotation/CSC. Manually control the IC output/display input buffer ready flags in interrupt handler and control IC input buffer ready flags in timer handler.
MXC V4L2 output maintains numbers of buffers.
Users can show the buffer on one framebuffer by calling VIDIOC_DQBUF ioctrl and return the buffer to the kernel by calling VIDIOC_DQBUF ioctrl.

## Slide 104: Features of MXC V4L2 Output
IC bypass mode (using DP or DC channel)
CSC can be done, but no resizing or rotation can be done. Manually control the display output buffer ready flags in the interrupt handler.
MXC V4L2 output maintains numbers of buffers.
Users can show the buffer on one VIDIOC_QBUF VIDIOC_QBUF ioctrl.

## Slide 105: Features of MXC V4L2 Output
TM
IC horizontal split mode (using PP channel)
Resizing/rotation/CSC. Manually control the IC output/IC input (right stripe)/display input buffer ready flags in the interrupt handler and control IC input (left stripe) buffer ready flags in the timer handler.
MXC V4L2 output maintains the number of buffers.
Users can show the buffer on one framebuffer by calling VIDIOC_QBUF ioctrl and return the buffer to kernel by calling VIDIOC_QBUF ioctrl.

## Slide 106: Features of MXC V4L2 Output
TM
VDI-IC video deinterlacing mode (using PRP_VF channel)
Resizing/rotation/CSC can be done. Manually control the IC output/display input buffer
ready flags in interrupt handler and control IC input buffer ready flags in timer handler.
MXC V4L2 output maintains the numbers of buffers.
Users can show the buffer on one framebuffer by calling VIDIOC_DQBUF ioctrl and return the buffer to the kernel by calling VIDIOC_QBUF ioctrl.

## Slide 107: How do we integrate IPUv3 into MXC V4L2?
Based on analysis of the IPUv3 spec
What channel should we use for the framebuffer?
What channel should we use for V4L2 capture and V4L2 output?
IPU low-level API design – enable/disable channel, init/unit channel, init channel buffer, interrupt handler register interface…
Invoke IPU low-level APIs from the MXC V4L2 driver.
Ensure backwards compatibility in the IPU low-level APIs in cases
where the hardware has not changed dramatically.

## Slide 108
Use case Examples & Tips

## Slide 109: IPUv3 tips
Use VDOA
  For more efficient DDR access pattern
Refresh the display at the rate of the content
  For displays the perform frame rate conversion.
  Sometimes called 24P cinema
  Significantly reduces the amount of data read by IPU.

## Slide 110: IPUv3 tips
Buffer management
  IPU write channel needs a free buffer in the DDR to start writing data.
  If there’s no free buffer IPU’s internal FIFOs are filled, causing additional latencies
  Buffer management system should guarantee that there’re always a free buffer for IPU’s usage.
  IPU can start writing the data to that free buffer immediately avoiding
unnecessary

## Slide 111: IPUv3 tips
Move load from the IC
  Perform CSC (Color Space Conversion), in DP (Display Processor), and not in the IC. (Save memory bandwidth, and lower load on the IC).
  Move combining tasks to the VDIC (if not used as de interlacer)
  Consider the IC processing speed, for the tasks
    Resize – 2 cycles/pixel
    Combine – 2 cycles/pixel
    CSC – 3 cycles/pixel
Flipping an image (a.k.a 180º rotation)
  Use H-flip and V-flip transfers, done by IDMAC and IC, and not using the
IRT module.

## Slide 112: IPUv3 tips- Optimizing memory accesses
Optimize Pixel formats
  The larger the chunks of data are – the easier it is on the DDR
  The smaller amount of bursts – better for the memory bus system
  Choose the mode that works best for the specific use case and avoid the rest
Format | Amount of data per macro block | Burst size | DDR3 x64 BL | Amount of bursts per macro block | Target
YUV422 interleaved | 256 bytes | 16 bytes | 2 | 16 | Best: IPU => IPU; VDOA => IPU
YUV422 partial interleaved | 256 bytes | 8 bytes + 8 bytes | 1 + 1 | 32 | 
YUV422 non interleaved | 256 bytes | 8 bytes + 4 bytes + 4 bytes | 1 +1+1 | 48 | 
YUV420 interleaved | 256 bytes | 16 bytes | 2 | 16 | 
YUV420 partial interleaved (NV12) | 192 bytes | 8 bytes + 8 bytes | 1 + 1 | 32 | Best: VPU => VDOA (decode) Best: IPU => VPU (encode)
YUV420 non interleaved | 192 bytes | 8 bytes + 4 bytes + 4 bytes | 1 +1+1 | 48 | 

## Slide 113: IPUv3M tips
How to work efficiently with the memory system
  Use real time channels
    Marking IPU accesses with an AXI ID to bypass the PL301’s arbitration
  Lock feature
    issue a series of IPU bursts the belong to the same channel – better chance for DDR hit
  Conditional read
    If an alpha mask is provided to the overlay plane transparent pixels are not read from memory.

## Slide 114: IPUv3 tips
Recommended Display Connectivity
i .MX51 |  |  |  |  |  |  | 
IPU_DISP1 port | 24-bi t RGB |  | RGB666 | RGB565 | RGB555 | 24-bi t YCbCr | YCbCr4:4:4
DISP1_DAT0 | B0 |  | B0 | B0 | B0 | Y0 | Y0
DISP1_DAT1 | B1 |  | B1 | B1 | B1 | Y1 | Y1
DISP1_DAT2 | B2 |  | B2 | B2 | B2 | Y2 | Y2
DISP1_DAT3 | B3 |  | B3 | B3 | B3 | Y3 | Y3
DISP1_DAT4 | B4 |  | B4 | B4 | B4 | Y4 | Y4
DISP1_DAT5 | B5 |  | B5 | G0 | G0 | Y5 | Y5
DISP1_DAT6 | B6 |  | G0 | G1 | G1 | Y6 | Y6
DISP1_DAT7 | B7 |  | G1 | G2 | G2 | Y7 | Y7
DISP1_DAT8 | G0 |  | G2 | G3 | G3 | Cb0 | Cb0
DISP1_DAT9 | G1 |  | G3 | G4 | G4 | Cb1 | Cb1
DISP1_DAT10 | G2 |  | G4 | G5 | R0 | Cb2 | Cb2
DISP1_DAT11 | G3 |  | G5 | R0 | R1 | Cb3 | Cb3
DISP1_DAT12 | G4 |  | R0 | R1 | R2 | Cb4 | Cb4
DISP1_DAT13 | G5 |  | R1 | R2 | R3 | Cb5 | Cb5
DISP1_DAT14 | G6 |  | R2 | R3 | R4 | Cb6 | Cb6
DISP1_DAT15 | G7 |  | R3 | R4 |  | Cb7 | Cb7
DISP1_DAT16 | R0 |  | R4 |  |  | Cr0 | Cr0
DISP1_DAT17 | R1 |  | R5 |  |  | Cr1 | Cr1
DISP1_DAT18 | R2 |  |  |  |  | Cr2 | Cr2
DISP1_DAT19 | R3 |  |  |  |  | Cr3 | Cr3
DISP1_DAT20 | R4 |  |  |  |  | Cr4 | Cr4
DISP1_DAT21 | R5 |  |  |  |  | Cr5 | Cr5
DISP1_DAT22 | R6 |  |  |  |  | Cr6 | Cr6
DISP1_DAT23 | R7 |  |  |  |  | Cr7 | Cr7
DI1_PIN2 | HSYNC |  |  |  |  |  | 
DI1_PIN3 | VSYNC |  |  |  |  |  | 
DI1_PIN15 | DRDY |  |  |  |  |  | 
DI1_DISP_CLK | CLK |  |  |  |  |  | 

## Slide 115: IPUv3 - debug
IPU error interrupts & status bits
  IPU errors are reported on the IPU_INT_STAT_5, IPU_INT_STAT_6, IPU_INT_STAT_9 and IPU_INT_STAT_10 registers. The 1st debug step should be inspecting these bits
    A flickering display is normally a result of a system bus load (DDR).
    These will be reported as “new frame before end of frame error” on
IDMAC_NFB4EOF register.
    Bus loads that causes errors on the CSI side will be reported on *FRM_LOST* status bits
    Some of IPU internal signals can be routed to pins and measured using the IPU diagnostics unit. These can be used to capture errors/interupts and track internal flows. (the IOMUX needs to be configured to output the ipu_diagbus signals)

## Slide 116: IPUv3 - debug
IPU diagnostics unit
  Some of IPU internal signals can be routed to pins and measured using the IPU diagnostics unit.
  These can be used to capture errors/interupts and track internal flows.
  The IOMUX needs to be configured to output the ipu_diagbus signals.
Task status and flow control
  A frozen display is sometimes a result of wrong control of the buffer management within the IPU.
  The status of each flow controlled by the FSU can be monitored using the TASKS_STAT status registers.
  In some cases a user may track the BUF_RDY and CUR_BUF
indications of the flow to track the flow.

## Slide 117: Dual video-in use case example
Memory
IPU
DISPLAY
RGB, 60Hz
Vid in RGB
Vid in YUV
IC
(PP - copy)
YUV, 20Hz ITU 656
Rear-View Cam
2x
Temp
3x
Background
GPU
Instrumental Layer
DP
CSI
CSI
DI
Bypass path, depending on needs
Inverted
IC (VF)
Inverted
Inverted, 60Hz ?
Inverted, 60Hz ?
Temp is needed for cases BG freq > Vid one

## Slide 118: Playback, HD1080p H.264 HP –> Display
IPU
Memory
DC/DI
DP
IC
VDI
CSI
60 Frames per sec 30 Frames per sec
DISPLAY
Video 720p YUV 4:2:0
WXGA YUV 4:2:2
GUI RGBA 8888

## Slide 119: Dual Playback, HD720p H.264 HP –> WSVGA Display
IPU
Memory
DC/DI
DP
IC
VDI
CSI
DISPLAY
DISPLAY
Video 720p YUV 4:2:0
60 Frames per sec 30 Frames per sec
RGB 888
WSVGA YUV 4:2:2
GUI RGBA 8888

## Slide 120
Demo

## Slide 121
Q & A

## Slide 122
TM
© 2014 Freescale Semiconductor, Inc. | External Use
www.Freescale.com