## Slide 1
Introduction to GPUs and to the Linux Graphics Stack

## Slide 2
I - Hardware : Anatomy of a GPU
General overview
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 3
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
General overview of a modern GPU’s functions
Display content on a screen
Accelerate 2D operations Accelerate 3D operations Decode videos
Accelerate scientific calculations

## Slide 4
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
CPU
Flash ROM (BIOS)
Super I/O
Serial Port Parallel Port
Floppy Disk Keyboard Mouse
Northbridge
(memory controller hub)
Southbridge
(I/O controller hub)
IDE
SATA USB
Ethernet
Audio Codec CMOS Memory
controller
Generator
Graphics card slot
High-speed graphics bus (AGP or PCI
Express)
Chipset
Clock Front-side
bus
Memory bus
Memory Slots
PCI
Bus
PCI Slots
LPC
Bus
Internal Bus
PCI
Bus Onboard
graphics
Cables and ports leading oﬀ-board

## Slide 5
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
Hardware architecture
GPU: Where all the calculations are made
VRAM: Stores the textures or general purpose data Video Outputs: Connects to the screen(s)
Power stage: Lower the voltage, regulate current
Host communication bus: Communication with the CPU

## Slide 6
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 7
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
crtc0
VGA Encoder
Display Port Encoder
DVI Encoder
crtc1
VGA Conn
DP Conn
DVI Conn
Driving screens : the big picture
Framebuffer: The image to be displayed on the screen(VRAM) CRTC: Streams the framebuffer following the screen’s timings Encoder: Convert the CRTC’s output to the right PHY signal Connector: The actual connector where the screen is plugged

## Slide 8
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
Screen connectors
VGA: Video, introduced in 1987 by IBM
DVI: Video, introduced in 1999 by DDWG
DP: Video & Audio, introduced in 2006 by VESA
HDMI: Video & Audio, introduced in 1999 by HDMI Founders

## Slide 9
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
HBlank
Line 0
Line 1
Line Y - 1
Line Y
CRTC Scanout
VBlank
HBlank
HBlank
HBlank
Line Y - 2
Driving screens : the CRT Controller
Streams the framebuffer following the screen’s timings
After each line, the CRTC must wait for the CRT to go back to the beginning of the next line (Horizontal Blank)
After each frame, the CRTC must wait for the CRT to go back to the first line (Vertical Blank)
Timings are met by programming the CRTC clock using PLLs

## Slide 10
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
CRTC
Screen
Video
EDID
EDID signal EEPROM
VGA cable
Configuring the CRTC : Extended display identification data
Stored in each connector of the screen (small EEPROM)
Is usually accessed via a dedicated I2C line in the connector Holds the modes supported by the screen connector Processed by the host driver and exposed with the tool xrandr (see xrandr --verbose)

## Slide 11
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Driving screens
Example: Some display standards
1981 : Monochrome Display Adapter (MDA)
text-only monochrome
720 * 350 px or 80*25 characters (50Hz)
1981 : Color Graphics Adapter (CGA)
text & graphics
4 bits (16 colours)
320 * 200 px (60 Hz)
1987 : Video Graphics Array (VGA)
text & graphics
4 bits (16 colours) or 8 bits (256 colours) 320*200px or 640*480px (<= 70 Hz)

## Slide 12
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Host < − > GPU communication
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 13
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Host < − > GPU communication
Modern host communication busses
1993 : Peripheral Component Interconnect (PCI)
32 bit & 33.33 MHz
Maximum transfer rate: 133 MB/s
1996 : Accelerated Graphics Port (AGP)
32 bit & 66.66 MHz
Maximum transfer rate: 266 to 2133 MB/s (1x to 8x)
2004 : PCI Express (PCIe)
1 lane: 0.25 − > 2 GB/s (PCIe v1.x − > 4.0)
up to 32 lanes (up to 64 GB/s)
Improve device-to-device communication (no arbitration)
Features
Several generic configuration address spaces (BAR) Interruption RQuest (IRQ)

## Slide 14
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Host < − > GPU communication
Programming the GPU : Register access via MMIO
A GPU’s configuration is mostly stored in registers;
A register is usually identified by an address in a BAR; We can then access them like memory;
This is called Memory-Mapped Input/Output (MMIO).
Another
process's memory
0
0xﬀﬀﬀﬀ
Disk RAM PCI-01:00 BAR0
0
0xﬀﬀﬀ
Unused
Unused
GPU 0, BAR 0
Register Space
0
0xﬀﬀﬀﬀ
(swap)
Logical address
Physical address
Example of a CPU process's virtual memory space

## Slide 15
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Host < − > GPU communication
GTT/GART(references RAM)
Location of the address/memory: CPU GPU RAM
Device
BAR 0
BAR 1
...
Physical address
GART
GPU virtual address (VRAM + GART)
GTT/GART
Providing the GPU with easy access to the Host RAM
Process virtual address space (VM)
GART as a CPU-GPU buffer-sharing mechanism
A program can export buffers to the GPU: Without actually copying data (faster!);
Allow the GPU to read textures & data from the program;

## Slide 16
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 17
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
The GPU needs the host for:
Setting the screen mode/resolution (mode setting); Configuring the engines and communication busses; Handling power management;
Thermal management (fan, react to overheating/power); Change the GPU’s frequencies/voltage to save power;
Processing data:
Allocate processing contexts (GPU VM + context ID); Upload textures or scientific data;
Send commands to be executed in a context.

## Slide 18
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
Overview of the components of a graphics stack
A GPU with its screen;
One or several input devices (mouse, keyboard);
A windowing system (such as the X-Server and Wayland); Accelerated-rendering protocols (such as OpenGL); Graphical applications (such as Firefox or a 3D game).
Components of the Linux Graphics stack
Direct Rendering Manager (DRM) : exports GPU primitives; X-Server/Wayland : provide a windowing system;
Mesa : provides advanced acceleration APIs;

## Slide 19
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
General overview
Kernel space
User space
Applications
Hardware
drm
radeon
intel
nouveau
GPU
Xorg
xlib
network x-server
libdrm
ddx
mesa
CPU
Rasterizer
If UCS*
Qt
gtk
nexuiz

## Slide 20
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
DRM and libdrm
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 21
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
DRM and libdrm
Direct Rendering Manager
Inits and configures the GPU; Performs Kernel Mode Setting (KMS); Exports privileged GPU primitives:
Create context + VM allocation; Command submission;
VRAM memory management: GEM & TTM; Buffer-sharing: GEM & DMA-Buf;
Implementation is driver-dependent.
libDRM
Wraps the DRM interface into a usable API;
Is meant to be only used by Mesa & the DDX;

## Slide 22
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Mesa
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 23
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Mesa
Mesa
Provides advanced acceleration APIs:
3D acceleration: OpenGL / Direct3D
Video acceleration: XVMC, VAAPI, VDPAU
Mostly device-dependent (requires many drivers); Divided between mesa classics and gallium 3D;
Mesa classics
Old code-base, mostly used by drivers for old cards;
No code sharing between drivers, provide only OpenGL;
Gallium 3D
Built for code-sharing between drivers (State Trackers);
Pipe drivers follow the instructions from the Gallium interface; Pipe drivers are the device-dependent part of Gallium3D;

## Slide 24
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Mesa
Applications
Mesa
State Trackers
pipe drivers
Mesa Classics
Weston
egl
x-server
xorg
mplayer
VDPAU
xonotic
libgl
Qt
OpenGL
intel
radeon
nouveau_vieux
swrast
Gallium
softpipe
llvmpipe
r600g
r300g
nvc0
nv50
...
nv30
CPU
LLVM
GPU
(through libdrm)

## Slide 25
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 26
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11
X11 and the X-Server
X11 is a remote rendering API that is 25 years old;
Exports drawing primitives like filled circles, lines;
Is extensible via extensions: eg. DRI2, composite, AIGLX.
The X-Server
Implements the X11 protocol and provides extensions;
Needs a window manager to display windows (like compiz); Holds 2D acceleration drivers (DDX): nouveau, radeon, intel; Logs in /var/log/Xorg.0.log (check them for errors).
The X Resize, Rotate and Reflect Extension (XRandR) Common X API to configure screens and multi head; Implemented by the open and proprietary drivers;

## Slide 27
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11
Reaction to an input event
1: The kernel driver evdev sends an event to the X-Server; 2: The X-Server forwards it to the window with the focus; 3: The client updates its window and tell the X-Server;
4 & 5: The X-Server lets the compositor update its view; 6: The X-Server sends the new buffer to the GPU.

## Slide 28
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Wayland
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 29
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Wayland
Wayland
Protocol started in 2008 by Kristian Høgsberg; Aims to address some of X11 shortcomings; Wayland manages:
Input events: Send input events to the right application; Copy/Paste & Drag’n’Drop;
Window buffer sharing (the image representing the window);
Wayland Compositor
Implements the server side of the Wayland protocol;
Talks to Wayland clients and to the driver for compositing; The reference implementation is called Weston.

## Slide 30
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Wayland
Reaction to an input event
1: The kernel driver evdev sends an input event to “Weston”; 2: “Weston” forwards the event to the right Wayland client; 3: The client updates its window and send it to “Weston”;
4: Weston updates its view and send it to the GPU.

## Slide 31
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11 vs Wayland
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 32
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11 vs Wayland
X11 vs Wayland
Rendering protocol vs compositing API:
X11 provides old primitives to get 2D acceleration (such as plain circle, rectangle, ...);
Wayland let applications render their buffers how they want;
Complex & heavy-weight vs minimal & efficient:
X11 is full of old and useless functions that are hard to implement;
Wayland is minimal and only cares about efficient buffer sharing;
Cannot realistically be made secure vs secureable protocol.

## Slide 33
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
X11 vs Wayland
X11 : Security
X doesn’t care about security and cannot be fixed: Confidentiality: X applications can spy other applications; Integrity: X applications can modify other apps’ buffers; Availability: X applications can grab input and be fullscreen.
An X app can get hold of your credentials or bank accounts! An X app can make you believe you are using SSL in Firefox!
Wayland : Security
Wayland is secure if using a secure buffer-sharing mechanism; See https://lwn.net/Articles/517375/.

## Slide 34
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Attributions
Outline
1
2
- Hardware : Anatomy of a GPU General overview
Driving screens
Host < − > GPU communication
- Host : The Linux graphics stack General overview
DRM and libdrm Mesa
X11
Wayland
X11 vs Wayland
3
Attributions Attributions

## Slide 35
I - Hardware : Anatomy of a GPU
II - Host : The Linux graphics stack
Attributions
Attributions
Attributions : Anatomy of a GPU
Moxfyre: https://en.wikipedia.org/wiki/File: Motherboard_diagram.svg
Boffy b: https://en.wikipedia.org/wiki/File: IBM_PC_5150.jpg
Katsuki: https://fr.wikipedia.org/wiki/Fichier: VGA_plug.jpg
Evan-Amos: https://fr.wikipedia.org/wiki/Fichier: Dvi-cable.jpg
Evan-Amos: https://en.wikipedia.org/wiki/File: HDMI-Connector.jpg
Andreas -horn- Hornig: https:
//en.wikipedia.org/wiki/File:Refresh_scan.jpg
Own work: https://en.wikipedia.org/wiki/File: Virtual_memory.svg